## Slide 1: Data Repositories for Parametric Workflow Models
Using model libraries in Teamwork Cloud to store and retrieve SIS and Launch Vehicle data

## Slide 2: Mission Integration: The Acoustics Problem
Acoustic loads create tremendous mechanical stresses on the entire launch vehicle.
This acoustic environment occurs in two stages –
1) hold down, when all the first stage engines are firing and building thrust, followed by
2) lift-off when the rocket actually starts to fly.
Potential areas of interest

## Slide 3: Converting Acoustic Signal into Sound Pressure Levels
Calculate the total energy contained in the spectrum, E =  S(f) df
Calculate Overall Sound Pressure Level, OASPL = 10*log10(E) [units: dB]
OASPL = 10*log10(E) [units: dB]
Measurement of acoustic signal in time domain (test lab, simulation, or other technique)
Converting time signal to frequency domain. Compare curves from different references and vehicles.
SIS provides general guideline as an envelope which constrains this freq curve.
Integrate under freq curve to find Overall Acoustic Sound Pressure Level (OASPL)

## Slide 4: Acoustics Algorithm
Measure or Predict
  20 in from PL Skin
PL Under Consideration
SIS Categories
(GovCloud)
LV Under Consideration
(LSP Cloud)
Assumptions
  P95/50 (95% Probability with 50% Confidence)
  PL shall be designed to tolerate the acoustic levels generated by LV
  From liftoff through SV separation
  Reference pressure 20 μPa
Workflow Steps
  Obtain V(t) [voltage time trace from microphone]
  Calc p’(t) = mic.constant * V(t)
    where p’(t) = pressure fluctuation
  Normalize p’(t) using reference pressure 20 μPa
  Calc S(f) using FFT
    where S(f) = spectrum of normalized p’(t)
  Correct S(f) for mic response and atmospheric absorption
  Compute Sound Pressure Level (SPL) Spectrum
    SPL(f) = 10*log10(S(f)) [units: dB/Hz]
  Compute Overall Sound Pressure Level (OASPL)
    E =  S(f) df [total energy contained in the spectrum]
    OASPL = 10*log10(E) [units: dB]
  Identify SPL and OASPL exceedances
Summary of main steps
Payload SPL vs freq submitted as raw data file, then imported into SysML table
Freq points from other vehicles and/or references
Freq curves juxtaposed to reveal crossing points, underlaps and overlaps
OASPL results shown on dashboard as a bar chart

## Slide 5: Workflow Analysis Model Structure

## Slide 6: Mission Integration Enterprise Internal Connectivity
Workflow model draws launch vehicle and interface specs from TWC data models
Payload data is read in via Excel interface with Cameo

## Slide 7: SIS Library Model

## Slide 8
SIS data model could be part of the actual requirement set, or a separate model for each workflow.
SIS data model is an online server project in Teamwork Cloud
Structure similar to UAF Logical Data Model (LDM)
Acoustic envelope data stored as instances

## Slide 9
Instance table for SIS data model - acoustics

## Slide 10: Launch Vehicle Library Model

## Slide 11
Separate TWC library model for each launch vehicle
Packages and data elements for LV variants based on workflow

## Slide 12
Falcon 9 (> 4k lbs) acoustics and loads instance tables

## Slide 13: Project Usages
Each library is brought into the acoustics workflow model as a “used project”

## Slide 14: Using the Library Models

## Slide 15
Empty instance table in acoustics workflow parametric model
Column headings correspond to value properties in the blocks
Step 1

## Slide 16
These columns will be populated with SIS data
This column is synced to Excel file for payload input data
This column will be populated with instance data from the LV library
Step 1

## Slide 17
PLTemplate.xlsx file attached to Cameo model
Step 2
Read in payload data from synced Excel file

## Slide 18
Step 2
Read in payload data from synced Excel file

## Slide 19
Step 3
Open read-only instance table from LV library
Copy sound pressure levels for Falcon 9 > 4k lbs (East)
Paste into splLVf9gt4kE column of analysis instance table

## Slide 20
Step 4
Open read-only instance table from SIS data model library
Copy sound pressure levels for Payload Categories A, B and C

## Slide 21
Step 4
Analysis instance table is nearly ready to run the simulation. Final step is to add an instance to receive the sums of the SPL transforms to calculate OASPL

## Slide 22
Parametric diagram calculates differences between PL SPL profile and SIS and LV profiles and notes exceedances
Parametric diagram also calculates transforms of each instance of SPL value
Carat symbol signifies these value properties inherited from used project

## Slide 23
OASPL Parametric diagram sums the SPL transform instances and converts them into OASPL values

## Slide 24
Differences calculated
TRUE checked if exceedance exists
Overall Sound Pressure Level values for payload, launch vehicle and SIS payload fairing categories

## Slide 25: Export Results to Attached Excel File
Differences and exceedances in red
Graph displays OASPL values

## Slide 26: Questions?