## Slide 1: "Physics, Systems Engineering, and the AtmoSniffer"
John E. Sohl
Weber State University, Physics

## Slide 2: A Shameless Plug for Weber State!
Physics (B.S.) & Applied Physics (B.S.)
  HARBOR near-spaceflight program
  One of the most hands-on physics programs in the US
  Alumni in “all” fields: Semiconductor design, aerospace, business, environment, nuclear energy & waste, national labs, universities, etc.
  Truth: All engineering is based on physics
Engineering (B.S., M.S.)
  Electrical, Mechanical (B.S. only), Computer
Manufacturing Systems Engineering (B.S.)
  Just started Fall 2018
  ~20 declared majors in the first year!

## Slide 3: Key Elements of Systems Engineering
Upfront Systems Engineering:
  Spending money early saves money later.
Rapid Prototyping:
  Learn from simple models and sub-projects.
    MSA, Mini-MSA, Tricorder, Mini-Beacon, etc.
Design for Manufacturability:
  Ease of assembly, relationship between parts, assembly sequence
Design for Maintainability
Enterprise Value:
  Market research to establish user needs.
Integration, Test, and Validation:
  Continuous calibration of prototypes

## Slide 4: Werner Gruhl’s famous NASA analysis

## Slide 5: From Bahill (2010) and INCOSE
The SIMILAR Process

## Slide 6: What is the AtmoSniffer?
Lightweight: < 1.4 kg
Compact: Loaf of Bread
Low Power: Runs 7 hours on 5200 mAh battery
Measures:
  CO, CO2, NO, NO2, SO2, NH3, O3, VOCs
  Particulate Counter: 1 µm to 10 µm
  Temp., Press., %RH, GPS Location (wind)
  9-axis inertial sensor (turbulence)
Multiple Interfaces
  Onboard datalogging to microSD
  Wi-Fi, Bluetooth, 900 MHz, Cellular
  Simple onboard display/buttons

## Slide 7: The Problem
Existing Air Quality Stations
  Large, heavy, expensive; but very accurate, high precision, low drift
  Typically one gas is measured
  Needs trained workforce to operate
  Needs AC power
$2M = 300+ AtmoSniffers

## Slide 8: Motivation
Ozonesonde/Radiosonde
Compact Modern Sensors
Need for a Full Data Set
Multiple Flight Platforms
Need for agile mounting

## Slide 10: Problems?
Pushing sensors to their limits
  Low level measurements & precision
  Oxygen starvation at high altitudes
  Response times and flight
  Cross-species sensitivity
Moisture affects calibration
Ambient Temperature affects calibration
Calibrating for Pressure
Surface chemistry
RF Noise
Oxygen starvation
Sensor zero-drift

## Slide 11: The Basic Idea

## Slide 12: Reality

## Slide 13: Just so you know where we are at…
The user interface
Some Calibration Results
Some actual flight data

## Slide 18: Ozonesonde vs. AtmoSniffer (90 min apart)
Ozonesonde is calibrated for pressure.
AtmoSniffer is raw data, without pressure correction.

## Slide 19: Problem Solving at Each Table!
Your task: The project is nearly ready for market, where would you put your final efforts? Why?
Suggestions for Conversation:
  Manufacturability
  Software
  User Interface
  Alpha and Beta Testing
  Signal Noise, Electronics, Calibration
  Housings: internal (function) and external (appearance)
  Other?

## Slide 20: So, what have you?