## Slide 1
Case Study:
Lid Installing Robot (LIR)
Lou Wheatcraft
Wheatland Consulting, LLC
Wheatland.consulting@gmail.com
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.
Notes: INSTRUCTOR NOTE: On day 2 and on day 3, begin the day with a question that the teams answer: What did you learn yesterday -- seven things -- write on your flip chart. Everyone reports back as a team
Be sure to cover the format for the class while this slide is up. Lecture and workshop. Working in teams. Learn not just from us but from each other.
Also if someone else has not done so, handle logistics – time for lunch, breaks, where are the bathrooms.
Frame:Them:
  How many of you have had to write requirements in the past? Comment on show of hands
  How many of you have had to do something with someone else’s requirements?
Comment usually is “well that covers most everyone”.
  How many of you have enjoyed either process?
Now comment that there are not any hands raised.
The problem is that writing good requirements is hard work. Writing bad requirements is hard work too. This class will help you do a better job of writing good requirements and avoid the writing of the bad requirements and then writing them over and over and over.
Do introductions: Name, area you work in, role in requirements definition,
  Note: RGI was supposed to require each of the students to state their expectations for the class and then RGI was to compile these and provide them to CAI before the class. Assuming this is done, you don’t need to ask for expectations as part of the introduction. Instead make up a summary slide from the material the students provided and update the one at the end of this presentation with those. Then on the next chart you can display this slide. (Insert a link on the word “expectations” and link to your expectations slide at the end. With the slide at the end, you can also then review these expectations again at the end of the class.)
US: [We establish our credibility as part of our introduction. Why are we qualified to teach this class?]
Message: This list of problems/expectations, represents problem areas that prevent you from delivering a winning product – a product provides what is needed, that is within budget, on time, and with the expected quality. This class will help you address these problems and deliver a winning product.
Ask for a show of hands - how long have you worked here? Less than 5 years? More than 20 years? Everyone else (5 – 20 years)?
Some of you may know a lot of this material already, however, many others that you work with may not. You need to become a mentor and teach them this kind of material.

## Slide 2: Background
Our business consists of production facilities where customer supplied products are put into jars of various sizes, labels applied, lids installed, and filled jars are packaged.
Filled jars are packaged 12 jars/package and packages are placed on pallets for customer pickup.
There are 10 production facilities spread across the country
  Each production facility has 20 Jar Processing Systems (JPS).
  Each JPS consists of the systems shown below. The Command & Monitoring (C&M) software runs on a computer system in a central Facility Control Room (FCR) with an operator to monitor each of the 20 JPSs visually via cameras and the FCR C&M software as well as monitor overall facility operations (fire, security, shipping/receiving, storage, HVAC, power).
  The actual number of JPSs in operation and number of jars to be filled each shift depend on customer demand – currently we are operating at maximum capability.
  The operating shift for the JPSs are 8 hours/day, 7 days/week, 355 days/year (10 days off for holidays). (Operations are constrained to only 1 shift per day.)
  All systems have been automated except the Lid Installation System (LIS).
Mom’s Best Sauce
JPS: Jar Processing System; FCR: Facility Control Room; C&M: Command & Monitoring

## Slide 3: Background
There is one LIS for each JPS.
  Currently, the LIS consists a separate, environmentally controlled room with an opening at one end to access the jars on the conveyor belt and a human lid installer to install the lids.
  The 8-hour shift consists of 7 hours of operations (actual lid installation) with two 15 min breaks and one 30 min lunch break.
  The human lid installers at each LIS can install one lid ~ every 3 min (140 lids/8-hour shift).
  This allows for a maximum daily capacity of 2800 jars filled/shift for each production facility (20x140).
Lids of the proper size are supplied to each LIS prior to shift start in boxes.
  Each JPS is assigned to a specific product and jar size.
  There are a variety of jars of varying heights, lid sizes, and materials (glass or plastic).
Jars are delivered to each LIS by JPS via the Conveyor Belt System.
  The human lid installers install the supplied lids on the jars to the proper torque specified by the jar manufacturer based on lid size and jar material.
  Lids are installed using a special lid installation tool with an indication of the amount of torque being applied.
  This is a two-hand activity, one hand holding the Jar in place while the other hand installs the lids using the installation tool.
LIS: Lid Installation System; JPS: Jar Processing System; FCR: Facility Control Room; C&M: Command & Monitoring
Mom’s Best Sauce

## Slide 4: Acquisition Concept
Our approach is to issue a contract based on an integrated set of needs for the Lid Installing Robot (LIR) that will replace humans as part of the LIS.
  The LIRs can work faster, are more efficient, and do not need to take breaks during a shift.
  Total cost per lid installed will be reduced increasing profit per jar.
  Automating lid installation will enable us to increase capacity, increase overall performance, meet projected increases in customer demand, and increase profit.
  Assumption is that there are Off-the-Shelf (OTS) automation solutions (robots) in the marketplace that can meet our needs.
We don’t have a dedicated Systems Engineering (SE)/product development team; so we hired River North Consulting to help us through the SE activities and analysis needed that will enable a clear definition of needs for which we can use during acquisition and include in a contract as well as validate the LIRs against.

## Slide 5: Acquisition Concept
River North will lead us through a series of steps defined in the INCOSE NRM and GtNR resulting in both an integrated set of needs as well as the underlying analysis from which the needs can be derived.
River North will work with our procurement/contracting personnel to prepare the contract, Statement of Work (SOW) or Supplier Agreement (SA) and do the technical evaluation of the proposals submitted.
River North is responsible for independent verification and validation of the supplier work products (design input requirements, design, design output specifications, production verification).
River North is also responsible for final system validation within one of our production facilities to ensure our needs have been met.
  Will use a dedicated JPS using a variety of jars and corresponding lids.
  Supplier will provide validation LIRs for these activities.
River North will provide recommendations concerning the acceptance of the LIRs.
Once the validation LIRs pass system validation and acceptance, the supplier will be authorized to provide the LIRs needed for our 10 production facilities (200 LIRs, plus spares, and spare parts.)
LIR: Lid Installing Robot; NRM: Needs and Requirements Manual; GtNR: Guide to Needs and Requirements

## Slide 6: Activities Involved
From INCOSE RWG NRM

## Slide 7
Identify the Problem/Opportunity;
Define Mission, Goals, Objectives

## Slide 8: 4.3.1 Define the Problem, Threat, or Opportunity
Enables the project team to understand why the project is worth doing, the system is needed, and the capabilities, functions, performance, and features that are important to the customers, users, and operators of the system.
The steps to defining the problem or opportunity include:
Identify the organization’s strategic and business operations level stakeholders that are impacted by the problem or threat or those who will benefit by pursuing the opportunity.
Work with of these stakeholders to understand how they are impacted by the problem or threat or those that will benefit by pursuing the opportunity.
Clearly define a statement of the problem, threat, or opportunity.
Get stakeholder agreement for the problem, threat, or opportunity statement.

## Slide 9: Problem Statement Analysis
Issues with current human lid installers
  Human lid installers get bored and are easily distracted.
  Some show up to work late, others take longer than allowed breaks.
  Some are even complaining about Carpal Tunnel Syndrome (CTS).
  The rate of lid installation by humans is limited to ~one lid every 3 min “on average”.
    Human installers frequently fail to properly install lids (lower yield).
  The net result is we are lucky to get 70% of the lids installed per shift per JPS.
  Unable to meet customer demand, resulting in unhappy customers.
  Revenue and profit is not what it could be.
Overall demand for our services is increasing
  Our marketing department says we need increase our capacity by over 6 times to meet projected demand.
    There are hard constraints limiting operations to 1 shift/day.
  The JPSs at each production facility have been undergoing automation needed to increase capacity so they will be capable of filling, labeling, and packaging jars at a rate to meet this demand.
  The bottleneck is the limited rate (and low yield) of current human lid installers.
LIS: Lid Installation System; JPS: Jar Processing System; FCR: Facility Control Room;

## Slide 10: Problem Statement
“Manual installation of lids is severely limiting the number of jars that can be processed, which prevents us from meeting the needs of our customers and maximizing our profit.”

## Slide 11: 4.3.2 Define Mission, Goals, Objectives, & Measures
The mission statement defines the “why” - why does the project exist? What does the organization’s strategic and business operations level stakeholders or the customer need to be accomplished? “What is the expected outcome?”
Goals are elaborated from the mission statement communicating those things that need to be achieved that will result in achieving the mission.
Objectives are elaborated from the goals providing more details concerning what must be done to meet the goals that will result in the mission to be achieved.
Measures are used to both validate the objectives against as well as to manage system development across the lifecycle.
Achievement of the MGOs and measures should result from the achievement of the integrated set of needs defined for the SOI.

## Slide 12: Mission, Goals, Objectives Business Perspective (of overall JPS automaton effort)
Mission Statement
  BM1: Maximize profit
Goals
  BG1: Automate entire JPS
  BG2: Reduce per jar processing cost
  BG3: Increase capacity (number of jars processed)
  BG4: Increase performance (yield)
  BG5: Retrain as many existing human workers as practical to fulfill new roles associated with automation and other activities within the facility
Objectives/Measures
  BO1: Procure automated JPS systems (BG1)
  BO2: Reduce the per jar processing cost by [TBD 50%] (BG2)
  BO3: Increase the daily capacity at each production facility by a least [TBD 600%] (BG3)
  BO4: Increase performance yield to [TBD >= 99%] for each production facility (BG4)
  BO5: Retain at least [TBD 35%] of current human workers (BG5)

## Slide 13: Mission, Goals, Objectives LIR Perspective
Mission Statement
  RM1: Provide a faster and more effective way to install lids on jars (BM1)
Goals
  RG1: Automate lid installation (BG1)
  RG2: Increase number of lids installed per shift (BG3)
  RG3: Increase yield (BG4)
  RG4: Minimize cost of implementation (BG2)
  RG5: Conduct safe food handling, hazardous materials handling, and robotic operations
Objectives
  RO1: Procure LIRs to install lids – Commercial off the Shelf (COTS) if possible (RG1) (BO1)
  RO2: Increase daily capacity to install lids to > [960 TBD] lids/shift for each JPS (RG2)(BO3)
    19,200 per shift (20 x 960) for each facility
  RO3: Increase yield such that the number of jars successfully installed per shift at each production facility is >= 99% (RG3)(BO4)
  RO4: Limit changes to existing facilities and processes (RG4) (BO2)
  RO5: Stay within the acquisition budget (TBD) (RG4) (BO2)
  RO6: Comply with OSHA robotics regulations (RG5)
  RO7: Comply with FDA food handling regulations (RG5)
  RO8: Comply with EPA hazardous materials regulations (RG5)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room;

## Slide 14
Identify the Stakeholders;
Stakeholder Perspectives;
Elicit Stakeholders’ Needs & Expectations; Document Assumptions

## Slide 15: 4.3.3 Identify External and Internal Stakeholders
Stakeholders are the primary source of needs and requirements
The choice of a relevant set of stakeholders is critical for being able to determine the completeness and correctness of the integrated set of needs and resulting design input requirements.
Stakeholders are any individual or organization with a personal stake in the SOI, who may be affected by the SOI, who will participate in the development of the SOI, are able to influence the definition and development of the SOI, or with whom the project team will interact across the SOI lifecycle.
A key part of stakeholder identification is to determine who the Approving Authorities are within the group of stakeholders.
There can be many stakeholders for a SOI over its lifecycle; therefore, considering the lifecycle concepts across the lifecycle provides a thorough source for stakeholder identification.
It is important to go beyond just users and the customer – rather than voice of the customer (VOC), think VOX

## Slide 16: Stakeholders for Customer/Supplier Perspectives
If you are a supplier, you will have internal organizational stakeholders as well as the customer.
Key things to consider:
Form, level, and quality of needs and requirements supplied by the customer
Access to customer internal stakeholders
Access to underlying analysis from which the needs or requirements were defined.
From INCOSE RWG NRM

## Slide 17: Include Higher-Level Business Stakeholders
These higher-level business lifecycle concepts, needs, and requirements constrain the system level lifecycle concepts, needs, and requirements.
To be successful, business stakeholders’ needs and requirements must also be considered
There are stakeholders at each level who have real-world expectations concerning a problem or opportunity and expected outcomes.
From INCOSE RWG NRM

## Slide 18: Flow Down, Allocation, & Budgeting
The receiving entities must define lifecycle concepts, needs, and design input requirements consistent with and trace to those of the parent entity.
Subsystem level Design Input Requirements flow down to the System Elements at the next level of the architecture via allocation and budgeting.
System level Design Input Requirements flow down to the Subsystems at the next level of the architecture via allocation and budgeting.
From INCOSE RWG NRM
The allocated parent requirements are constraints to the receiving entities they were allocated to.

## Slide 19
Identify the Stakeholders

## Slide 20: Identify Key Stakeholders – LIR Project Internal & External
S1: Me, Company Owner (Internal)
S2: Customers (External)
S3: Ronald Roundtop, Chief of Operations (Internal)
S4: Tom Torque, Facility Manager (Internal)
S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
S6: Sally Lidisan, Sales, Lids Unlimited, Inc. (External)
S7: Bob Jarhead, Sales, Jars Unlimited, Inc. (External)
S8: Mary Safelton, Chief Safety and Compliance (Internal)
S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
S10: Irene Teichmann, Chief of IT (Internal)

## Slide 21: Identifying Stakeholders – Are their others?
What about potential LIR suppliers?
    Can do a Request for Information (RFI), research marketplace, trade shows
What about the public?
    Represented by the regulators, our customers, and our “Office of Community Relations”
What about the regulators?
    Including fire marshal, we have an internal “Safety and Compliance Office” to address EPA, OSHA, FDA regulations
What about the knowledge of the lid installers being replaced?
    Technical view represented by chief of operations.
    Social perspective included in MGOs to retrain, repurpose as many as possible, help others find jobs, and provide financial support for during retraining
  Business stakeholders?
Others?
    During elicitation will ask if a stakeholder knows of any other stakeholders that should be included.
    When identifying external stakeholders, will ensure the stakeholders representing all external interfaces are included.
LIR: Lid Installing Robot; RFI: Request for Information; MGOs: Mission, Goals, Objectives; EPA: Environmental Protection Agency: OSHA: Occupational Safety and Health Administration; FDA: Food and Drug Administration

## Slide 22: Identifying Stakeholders – Business
Human Resources
  Repurpose human lid installers
  Training
  New Hires resulting from the automation
Finance/Budgeting
  Budgeting of funds to make all necessary changes: Facility upgrades, new personnel, training, procurement of LIRs and supporting infrastructure?
Procurement/Contracting
  Issue RFIs, prepare contracts/SOWs/SAs), issue RFP, evaluate proposals, select contractors.
    LIRs, Facility upgrades due to increased capacity.
  Update existing contracts due to increase in production (Lids, Jars, Labels, packaging, customers)
  Monitoring contract performance and deliverables
Office of Community Relations
  Impacts on local community: increased traffic, noise, pollution (emissions, wastewater, operating hours).
LIR: Lid Installing Robot; RFI: Request for Information; RFP: Request for Proposal; SOW: Statement of Work; SA: Supplier Agreement

## Slide 23
Stakeholder Perspectives

## Slide 24: Stakeholders’ High-Level Needs & Expectations
S1: Me, Company Owner (Internal)
  MGOs achieved within the drivers and constraints.
  Meet the customer demand for filled jars.
  Can the LIRs meet my MGOs and other needs?
S2: Customers (External)
  Facility can receive and store customer supplied product in bulk containers.
  Facility can properly handle, label, and fill jars with a variety of eatable food stuffs as well as non-eatable cleaning chemicals and compounds.
  Jars can be either glass or plastic.
  Lids are properly installed on the jars.
    Positive seal with a torque applicable to the size of lid and jar material.
  Meet customer demand for filled jars.
  Able to package and stage filled jars for pickup and delivery to customer’s customers.
  Facility cleans and makes available for pickup empty product bulk containers for reuse.
  Bottom line – can the LIR meet the customer lid installation requirements?
MGO: Mission, Goals, Objectives

## Slide 25: Stakeholders’ Needs & Expectations (2)
S3: Ronald Roundtop, Chief of Operations (Internal)
  No changes to existing LIS rooms
  Meet customer demand
  Lids installed on jars per customer specs
  Maximize yield per shift
  Keep company owner (boss) and customers happy
  Provide JPSs and associated LISs with daily quantity of product, jars, labels, and lids
  Workable LIRs are available during operational shift.
S4: Tom Torque, Facility Manager (Internal)
  Operations take place successfully within the existing space, operating environment, and power provisions in the facility & LISs
  Support IT’s needs concerning monitoring, command, and control of the LIRs.
  Able to safely handle and dispose of any spilled product (eatable as well as potentially hazardous non-eatable products).
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; IT: Information Technology

## Slide 26: Stakeholders’ Needs & Expectations (3)
S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
  Able to receive and safely store required quantities of product, jars, labels, lids, and packing and shipping materials
  Adequate storage capacity (warehouse space) for 2 weeks of product, jars, labels, lids, and packing and shipping materials
  Adequate space for staging filled jars for daily pick up by customer
  Receipt of LIRs that have survived the various shipping environments
  Store crated LIRs in the existing, non-climate-controlled storage facilities
  Adequate space for unused jars and lids to be returned to the suppliers
  Warehouse space will need to be increased due to increased throughput
S6: Sally Lidisan, Lids Unlimited, Inc. (External)
  Existing range of lid sizes will continue to be installed on the jars
  Ensure each facility has sufficient supply of lids of proper sizes
  Facility returns unused lids for repackaging and reuse
  Will need a contract change for increased supply of lids
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 27: Stakeholders’ Needs & Expectations (4)
S7: Bob Jarhead, Sales, Jars Unlimited, Inc. (External)
  Existing jar sizes will continue to be used
  Existing jar materials (glass or plastic) will continue to be used
  Lids are installed on the jars with the proper torque based on jar opening size and jar material
  Ensure the facility has sufficient supply of jars of proper sizes
  Facility returns unused jars for repackaging and reuse
  Will need a contract change for increased supply of jars
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 28: Stakeholders’ Needs & Expectations (5)
S8: Mary Safelton, Chief Safety, Quality, and Compliance (Internal)
  Safety
    LIRs are compliant with organizational standards for human system integration, workmanship, safety, quality, and labeling.
    LIRs comply with OSHA regulations concerning automations vs humans.
  Quality
    LIRs pass system validation: do the delivered LIRs meet our needs?
    LIRs pass system verification: do the delivered LIRs meet the agreed to supplier defined design input requirements?
    LIRs pass production verification: meet supplier defined output specifications - were the LIRs built to spec?
  Compliance
    Facility complies with FDA cleanliness and sanitation regulations concerning handling of human consumable products placed in jars.
    Facility complies with EPA safety regulations concerning handling and storage of non-eatable potentially hazardous chemicals placed in jars as well as handling of any spills and resulting wastes associated with cleanup of those spills.
LIR: Lid Installing Robot; EPA: Environmental Protection Agency: OSHA: Occupational Safety and Health Administration; FDA: Food and Drug Administration

## Slide 29: Stakeholders’ Needs & Expectations (6)
S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
  LIRs work reliability and have a long lifetime.
  Ensure LIRs are maintained properly for maximum performance per supplier provided procedures.
  LIRs require a minimum of maintenance.
  LIRs can be repaired easily and fast – inhouse with line-replaceable parts.
  LIRs can be moved within the facility with a single maintenance tech.
  Spare LIRs will be available to replace LIRs needing off-line maintenance or repair.
  Spare parts and materials are available to repair and maintain LIRs.
S10: Irene Teichmann, Chief of IT (Internal)
  Establish new data and command communications capability between LIRs and FCR
  Develop, test, & maintain new displays and associated LIR command and monitoring (C&M) software in the FCR.
  Maintain security protecting the facility and all JPS systems from outside access (hacking).
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 30
Document Assumptions

## Slide 31: Document Assumptions
The number of shifts will stay the same.
The hours of facility operation will stay the same.
The number of JPSs within the facilities will not change.
The operating environment within the LISs will remain the same.
The characteristics of the jars and lids delivered by the JPS to the LISs will not change.
Empty jars are cleaned and sanitized by the supplier prior to delivery.
The location of jars on the conveyer belt will not change.
Jars are sitting, unrestrained on the conveyer belt.
Jars will need to be held in place during installation.
During installation of the lids on the jars the LIRs will not change the location of the jars on the conveyer belt.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 32: Assumptions (2)
Timing will be adjusted to meet the performance needs of the JPS and customer product within maximum speed constraints.
  The JPS will notify the LIR when a jar is in place and ready for lid installation.
  The LIRs will be able to install lids on the jars per the defined jar delivery timing.
Daily supply of Lids of the proper size will be supplied to the LIS by a maintenance technician prior to shift start.
The LIS room will have sufficient space for containing the increased volume of a daily shifts worth of lids (960) and a method for delivering the lids to the LIR.
  The form in which the lids will be delivered and made available to the LIR is TBD.
The size of jars/lids will remain constant for a given shift for each JPS.
The existing FCR will be upgraded to allow command of the LIRs and and monitoring of the LIR health and status.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 33
Elicit Stakeholder Needs and Requirements

## Slide 34: 4.3.4 Elicit Stakeholder Needs & Requirements
Engage the stakeholders to understand their needs and technical requirements for the SOI not only just during operations but for all lifecycle stages.
The elicitation activities allow the project team to discover and understand what is needed, what processes exist, how stakeholders interact with SOI, what happens over the SOI’s lifecycle - good and bad, what states and transitions the SOI might undergo or experience during use, nominal, alternate-nominal, and off-nominal operations, and other considerations.
Each stakeholder has a unique perspective in terms of concerns, problems, challenges, issues, risk, opportunities, experience, failures, and successes.
During elicitation, the project team should collaborate with the stakeholders to understand the source and context (rationale) of their stated needs and requirements.
Techniques and methods used during elicitation include brainstorming, workshops, focus groups, interviews, document analysis, interface analysis, prototype analysis, observations of like products, questionnaires, site visits, models, and diagrams.
Successful elicitation results from proper planning on the methods and identification of the types of information to be obtained and specific questions to ask that will result in that information.

## Slide 35: Information needed from the stakeholders
Stakeholder perspective on how successful operations will be conducted once the LIRs are in place.
What changes will have to be made to the facility to accommodate the increase rate of lid installation?
What other systems or processes are affected by using the LIRs?
What are the drivers and constraints?
What could go wrong during operations?
What are the risks?
Are there any issues associated with automating the lid installation of the jars?
What are the stakeholders assuming for what they are telling us to be valid?

## Slide 36: Information needed from the stakeholders (2)
What do we need to know more about?
  Jars: size, required torque for lid installation, location of portion of jar the lid will be installed, best location to grasped the jar to keep the jar from rotating during lid installation.
  Frequency and position of jars delivered on the conveyor belt – JPS ICD.
  Operating shift: Actual number of hours per day, which hours? Number of days/year
  How do the LIRs know when the shift begins/ends? When a jar is in place?
  Lids: when, where, how delivered to LIRs, in what form, accessibility, location within the LIS.
  Lids: number, size, shape, grip locations, and allowable grip force.
  How will the LIRs be able to obtain the lids?
  Operational environment: temperature, humidity.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 37: Information needed from the stakeholders (3)
  Allowable induced environment by the LIRs: EMI/EMC, noise, thermal.
  Space within the LIS room.
  Power and quality of the existing power within the LIS?
  Location and size of the opening between the LIS and the JPS conveyer belt.
  LIR storage environment when not in the LIS room - crated and uncrated.
  Transportation/shipping environments.
  Expectations for safety, security, reliability, maintainability, lifetime, and other -ilities
  Interfaces/interactions of LIRs with JPS, LIS, FCR, operators, maintenance techs.
  Codes, regulations, standards the LIRs must be compliant.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 38: Methodology
Checklists were developed to ensure needed information was obtained
Individual interviews with stakeholders, group meetings, brain storming sessions.
Site visits – observed actual current operations of JPS, operations within the LIS rooms, shipping and receiving, storage facilities, and FCR.
Data recorded as operational scenarios, stories, and use cases
Data initially collected using standard office applications
Final data and information recorded within the RMT in a form to allow traceability.
Inconsistencies and discrepancies were noted, and effected stakeholders contacted to resolve these issues.
Results are shown in the following slides.

## Slide 39: Operational Scenarios, Stories, Use cases S3: Ronald Roundtop, Chief of Operations (Internal)
Location of key information
  Information on how LIRs interface (interact) with the JPS is defined in the JPS Interface Control Document (ICD)
  Information on how the LIRs interface (interact) with the LIS room is defined in the Facility ICD.
  Information on the characteristics of the jars is defined in Jar Spec 1245.
  Information on the characteristics of the lids is defined in Lid Spec 1246.
Nominal LIR Operations
  Start-up: Prior to shift start, a technician removes unused lids from LIS and provides a shift’s worth of lids (960) of the proper size to the LIS. Once the technician has left the LIS room, the LIR is powered up remotely by the operator in the FCR. Upon power up, the LIR completes a self-test and reports its health and status to the FCR as defined in the FCR ICD. The LIR positions itself to be ready to obtain a lid from the LDS and grasp the jar when commanded to do so.
  Lid Installation: The JPS presents jars (1 every 30 seconds, starting at 8 pm and continuing to 4 pm, 355 days per year) on a conveyer belt located on the other side of the LIS/conveyor belt system access opening. The JPS pauses each jar for 10 seconds for lid installation and takes up to 20 seconds for the next jar to be in place.
  At shift start, the JPS positions a jar in the LIS/ conveyor belt system access opening per the JPS ICD and sends the FCR C&M software a message that the jar is in place within 1 sec. The FCR C&M software notifies the LIR within 1 second of when the first and subsequent jars are in place for lid installation. The LIR will grasp the Jar to keep it from rotating and install the lid during the jar's pause with a torque as recommended in Table 3. Once the lid is installed, the LIR obtains another lid from the LDS and positions itself to be ready to grasp the next jar and install a lid.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 40: Operational Scenarios, Stories, Use cases S3: Ronald Roundtop, Chief of Operations (Internal)
Concurrent LIR Functions During Operations
  Commands: During lid installation operations, the LIR will always be listening for commands from the FCR C&M software. When a command is received, the LIR will execute the command, and report the execution of the command.
  Health & Status: During operations, the LIR will monitor system health and report any changes in status to the FCR C&M software . If a critical error is detected, the LIR will notify the FCR C&M software and perform the end-of-shift shutdown sequence. (A critical error is an error that could result in damage to the LIR, conveyor belt system, a person, the LIS room, or renders the LIR incapable of lid installation.)
  Change of state: The LIR will notify the FCR C&M software any time its state changes (Powered up, Self-test complete, Ready to install lids, Executing end of shift sequence, position, executing power down sequence). Changes of state can occur as a result of an internal software action or in response to a command from the FCR C&M software .
  Controlled Entry to the LIS: There is an interlock built into the LIS room door which will notify the FCR C&M software when the door is open, resulting in the FCR C&M software sending the LIR the “execute end-of-shift shutdown sequence” command as well as all other JPS systems. In addition, the LIS is monitoring for motion within the LIS space not occupied by the LIR. If for some reason the door interlock doesn’t work, and motion is detected within the LIS room; the LIS will notify the FCR of the detected motion which will trigger the FCR C&M software to send and “ execute end-of-shift shutdown” command to all JPS systems including the LIR.
LIR End-of-Shift Shutdown:
  The JPS stops jar processing operations at 4 pm local time. At this time, the LIR stops lid installation automatically based on its internal clock. The LIR shutdown sequence includes automatically ceasing lid installation, returning a lid to the LDS if it is holding one, positioning itself for start up for the next shift, notifying the FCR C&M software of its status & state, and powering itself down (sleep state, ready to accept a power up command.)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 41: Operational Scenarios, Stories, Use cases S3: Ronald Roundtop, Chief of Operations (Internal)
Facility Control Room (FCR):
  Current State: Operations within the FCR include monitoring the JPS, Fire Suppression System (FSS), access to all rooms, shipping & receiving, and facility HVAC.
  There are environmental sensors in all LIS rooms whose data is monitored from the FCR. From a security perspective, there are cameras in all operational areas.
  The FCR video system displays camera feeds from all operational areas, including the interior and exterior of the LISs.
  The FCR has undergone a recent upgrade in terms of controlling and monitoring the JPS systems which included new software applications and computer displays. Messages from the JPS systems to the FCR C&M software include messages to indicate operational status, power state, when a jar is in place for lid installation, and whether a jar has had a lid installed when the jar exits the LIS/conveyor belt system opening.
  There is also a facility-wide PA system in the FCR. The FCR C&M software maintains a status log for all JPS system activities, health, and status.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 42: Operational Scenarios, Stories, Use cases S3: Ronald Roundtop, Chief of Operations (Internal)
Facility Control Room (FCR):
  Future state: We plan to upgrade the FCR C&M software to add the capability to monitor and control the LIRs.
  The FCR C&M software will be able to command the LIRs as well as will receive state change messages and health & status data from each of the LIRs.
  The FCR C&M software will maintain a status display for the operator for all 20 LIRs in operation at a facility.
  We will also enable the FCR C&M software to send a “Jar in Place” (JIP) message automatically to each LIR. This will allow us to automate many of the routine lid installation tasks.
  The FCR C&M software will be capable of automated responses to minor LIR anomalies and notifying the operator (both audibility and visually) of critical anomalies.
  The FCR C&M software will also maintain a health and status log for each LIR. This log will record all commands sent to the LIRs and their acknowledgement, LIR H&S data, critical failures, changes of state, power up times, force used to grasp jars, number of lids installed, and torque applied to install lids as a minimum.
  All communications (commands, data, and messages) between the LIR and the FCR C&M software will be defined in the FCR to LIR ICD.
  Keypads will be added to control access to all LISs along with a MDS to detect motion within the LIS room. The FCR C&M software will monitor the keypad access to each LIS and the MDS. If someone enters the LIS or motion detected within the room, the FCR C&M software will send an end-of-shift shutdown sequence command to the LIR and all other JPS systems.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 43: Operational Scenarios, Stories, Use cases S3: Ronald Quench, Chief of Operations (Internal)
FCR operations (LIR):
  Nominal Operations with the LIR: 20 minutes prior to shift start, after the lids have been delivered to each LIS, the FCR C&M software will send a power up command to each LIR. Upon power up, each LIR will do a self-test and send its health status data to the FCR C&M software and notify the FCR software if a critical failure has been detected.
  During the shift, the LIRs will send periodic health and status updates to the FCR C&M software. If a critical failure is detected, the LIR will notify the FCR C&M software and execute the “end of shift shutdown sequence”.
  Assuming the LIR is powered up, its health status is set to “Ready to Install Lids”, has obtained a lid, and is in position install it on a Jar, the FCR C&M software will send the LIR a Jar-In-Place (JIP) message within 1 second of the first and each subsequent jar stopping in the opening.
  Upon receipt of the JIP message, the LIR will grasp the jar, move the lid to the jar, install the lid with the proper torque, release the jar, obtain another lid and and position itself ready to grasp the next Jar.
  End of Shift: The end of shift operations are automatic. At the end of shift, all JPS systems stop operations based on their internal clocks which are kept in sync with the FCR clock. The LIR will position itself for the start of the next shift, send an “end of shift shutdown success message” to the FCR C&M software, and then power down (go into a sleep state, ready to receive a power up command). The FCR C&M software will monitor each LIR to ensure the LIR end of shift shutdown sequence was executed successfully, powered down, change of state was successful, and notify the operator via a console display the state of each of the 20 LIRs.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 44: Operational Scenarios, Stories, Use cases S3: Ronald Quench, Chief of Operations (Internal)
Off Nominal Operations:
  If either a LIR or any other JPS system has a critical failure during the shift, the LIR will “Perform End-of-Shift Shutdown” and the FCR C&M software will send a “Perform End-of-Shift Shutdown” command to the JPS systems, alert the operator, and notify the maintenance technician on duty. The operator will also contact the maintenance technician directly to provide more information on what the problem is.
  If a fire is detected in a LIS area, the LIS Fire Suppression System (FSS) will automatically activate water sprinklers in the ceiling and the fire department will be notified without any FCR action. The FCR C&M software will also send a “Perform End-of-Shift Shutdown” command to the effected LIR(s) and other JPS systems. The LIR will need to survive a fire suppression event.
  If a person enters the LIS room during operations using the keypad, an interlock in the door will notify the FCR C&M software, which will immediately send a “Perform End-of-Shift Shutdown” command to the LIR and other JPS systems. Once the FCR gets confirmation that the LIR has ceased operations, the FCR will open the door. In addition to the door interlock, the LIS is continuously monitoring for motion within the LIS room (other than the the LIR). If for some reason the door interlock doesn’t work, this will result in the LIS notifying the FCR C&M software that motion was detected which will result in the FCR C&M software to immediately send a “Perform End-of-Shift Shutdown” command to the LIR and other JPS systems.
  The operator will assess the situation via the CCTV system and establish communications with the person entering the room via an intercom system. (Normally, the person should have notified the FCR operator of their need to enter the LIS area before doing so. This would allow the operator to send a “Perform End-of-Shift Shutdown” command to the LIR and other JPS systems prior to the person entering the LIS.) From a safety perspective, the LIS motion detection is primary, the door interlock is backup.
  If the FCR C&M software has a problem - failed communications with the LIR or FCR C&M software, computer freezing, etc. the FCR operator will issue a manual “Perform End-of-Shift Shutdown” command to the LIR all the JPS systems. The operator will then follow published procedures developed by the IT department to restore normal operations. If they fail to restore nominal operations, the operator will notify the IT department for assistance.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 45: Operational Scenarios, Stories, Use cases S4: Tom Torque, Facility Manager (Internal)
LIR Nominal Operations:
  All information concerning LIS room space, environment, and power provisions will be provided to bidders. Tables 1 & 2 show the existing environmental factors and Figures 1 & 2 show the LIS room layout and opening to the Conveyor Belt System.
  Operating environment: Each LIR is contained within the LIS room with an operating environment as defined in Table 1. Entry into the room is a standard 3-0 door located at the opposite end of the room from the opening to the Conveyor Belt System . The door is currently used by the human lid installer to enter and exit the room. Because of OSHA requirements, the door will remain closed and locked while the LIR is in operation.
  LIS room access: There will be a keypad access panel to each LIS room so only authorized personnel may enter. There will be a visual indicator outside the door whenever the LIR is powered up and active. If the door is opened, a signal will be sent to the FCR C&M software, which will in turn send a “Perform End-of-Shift Shutdown” command to the LIR and other JPS systems to cease operations. In addition to adding a keypad entry to the LIS, the LIS will be equipped with a motion detection system to detect motion within the LIS room. If motion is detected within the LIS room, a signal will be sent to the FCR C&M software, which will in turn send a “Perform End-of-Shift Shutdown” command to the LIR and other JPS systems to cease operations.
  Movement in/out of the LIS: The assembled LIRs will need to be able to be moved into and out of the LIS through the existing door by a single technician without the need for disassembly or the use of any special equipment
  Operating power for LIRs. There is standard 110-120-volt 30-amp power available with a URL standard 3 prong plug within 6 feet of the opening to the conveyor belt. The quality of the power is defined in the Facility ICD.
  Space for containing a daily shifts worth of lids (960) is limited to the existing floorspace within the LIS room.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 46: Operational Scenarios, Stories, Use cases S4: Tom Torque, Facility Manager (Internal)
Table 1 describes the operating environment within the LIS rooms. These temperature, humidity, dust, and lid installation values are typical for the work area within the LIS room and other operational areas within the facility.
Table 1: LIS Room Operating Environment
Environment Variable | Minimum | Maximum
Temperature | 55 deg F | 85 deg F
Humidity | 0 % | 30%
Dust | 0 | M8 (FED STD 209E)
Lighting | 10 foot/candles | 30 foot/candles
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 47: Operational Scenarios, Stories, Use cases S4: Tom Torque, Facility Manager (Internal)
Table 2 describes the emissions environment within the LIS rooms. These emissions are typical for the work area and other operational areas within the facility.
Table 2: Emissions within the LIS
Power (Volts/meter) | Frequency
20 V/m | 10kHz - 2 MHz
50 V/m | 2MHz - 200MHz
20 V/m | 10kHz - 2MHz
50 V/m | 2MHz - 10GHz
50 V/m | 200MHz - 18GHz
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 48: Operational Scenarios, Stories, Use cases S4: Tom Torque, Facility Manager (Internal)
Figure 1 provides a top view of the LIS room in which the LIR will operate. The corridor is a free space in which, if the LIR is mobile, the LIR may be placed and may move without encountering obstacles. All LIS rooms are the same. The JPS conveyer belt system is located on the other side of the LIS JPS access opening as shown on the drawing above and Figure 2. The location of the table where lids are currently placed for the human jar lighters is also shown. Once the LIR is operational, this table will be removed and replaced with a TBD Lid Dispensing System (LDS). The MDS is a new system to be added to the LIS room. 120 VAC, 30 amp power is available via a URL standard 3 prong receptacle.
Figure 1: LIS: LIR Operating Area – top view
JPS Conveyer Belt System
Access to jars is through a 3’ x 3’ opening (see Figure 2)
Table where boxes of lids are currently provided
3-0 Door
4’ x 8’ corridor, 8’ high
Keypad access panel
Room is 6’ Wide x 10’ Deep, and 8’ high
New Motion Detection System (MDS)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 49: Operational Scenarios, Stories, Use cases S4: Tom Torque, Facility Manager (Internal)
Each jar is be positioned on the conveyer belt within the opening as shown in Figure 2, where the jar is located halfway between the sides of the opening (18 inches from right or left side) and centered halfway back (9 inches) from either side of the conveyer belt with the following tolerances:  0.5 inch in each direction. The jar location on the conveyor belt during lid installation must not change.
Figure 2: Jar location within the JPS
36”
36”
36”
Conveyer Belt
18”
Opening into Conveyor Belt System
Note: Jar is centered in window when conveyer belt stops
Jars centered on conveyer belt
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 50: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
Receiving LIRs from supplier to production facilities:
  The supplier needs to ship the LIRs in crates.
  The environment during shipping is not controlled so these crates will need to protect the LIRs from external environments (loads, temperature, humidity, particulates) during shipping in the environmental conditions shown in Table 3.
  The LIRs may be shipped in pieces for assembly at the production facilities or shipped fully assembled if the crated dimensions are compatible (size & weight) with the size limits defined in Table 4.
    Initial shipping of LIRs from the supplier to the production facilities will be done by truck.
    Intermediate shipping may be by plane, boat, ship, or truck.
    Final shipping to the production facilities will be by truck.
    Forklifts may be used to transfer crated LIRs between shipping modes and at the production facilities.
  LIRs will be checked in at the production facilities receiving dock and crates inspected for damage prior to being moved via forklift to the LIR crated storage facility.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 51: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
LIR Crated Storage
  Initially the LIRs will be stored in their shipping crates in our LIR crated storage facility without climate control, on a concrete floor, under roof.
  Storage facility doors are open for many hours during the day and dust and high humidity are common with expected values shown in Table 5. Assumption: LIR shipping crates will protect the LIRs from the environment encountered during both during shipping and storage.
  Crates may be placed on supplier provided pallets off the floor.
Receiving (LIR spare parts)
  Spare parts received from the LIR supplier will be received, inspected, entered in the inventory control system, and then sent to the maintenance area for storage in a controlled environment having the characteristics specified in Table 1.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 52: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
Table 3 defines the expected shipping environment, along with the vibration loads, the crated LIRs are to be exposed to during shipping and handling.
Table 3: Shipping Environment
Environment Variable | Low | High
Temperature | - 80 deg F | 134 deg F
Humidity | 0 % | 100%
Vibration |  | [TBS]
Dust | 0 | M10 (FED STD 209E)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 53: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
Table 4 shows the weight and size limits for the LIR component packages. These restrictions only pertain to individual packages. There are no limits to the total weight of a shipment or the total number of packages in a shipment. The constraints are based on trucking, given the LIRs need to be delivered to the production facilities via truck. These limits are the more restrictive as compared to shipping via rail, plane, or ship.
Table 4: Shipping Package Size and Weight Limits
 | Maximum Allowed | Notes:
Weight | 150 lbs | Actual weight to nearest pound.
Combined Length & Girth | 165 in | Length + Girth (2x Width + 2x Height) to the nearest inch
Length | 108 in | Measure the longest side of the package, rounding to the nearest inch
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 54: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
Table 5 shows the storage environment within the unconditioned storage facility the crated LIRs will be exposed to.
Table 5: Storage Environment
Environment Variable | Minimum | Maximium
Temperature | - 30 deg F | 120 deg F
Humidity | 0 % | 100%
Dust | 0 | M10 (FED STD 209E)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 55: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
Receiving (Lids from the lid supplier after automating lid installation):
  Lids are received from the lid supplier boxed, 48 lids per box. The boxes are combined on pallets, 80 boxes per pallet (3,840 lids per pallet). Each day’s operations requires up to 5 pallets for a total of 19,200 lids per operating facility per day. (Before automation only 2800 lids were needed per day.)
  The lid supplier will will make weekly deliveries of 7 days worth of lids to each facility. This results in a weekly delivery of a maximum of 35 pallets per operating facility (7*19200 = 134,400 lids). (Before automation only 5 pallets were needed per week.)
  The lids delivered by the the lid supplier will have the characteristics specified in lid spec #LID1234.
  The actual number of lids needed may vary depending on customer demand. Orders for lids will be made at least one week prior to delivery.
Storage (Lids)
  The lids will be stored within the production facility in the storage environment defined in Table 1.
  Increasing from 5 pallets/week to 35 pallets/week will require an expansion of our storage facility to accommodate the increased number of pallets of lids (as well as the increased number of pallets of jars. In addition, we will need more forklifts and forklift operators to accommodate this increase in pallets.
Shipping (Unused lids back to lid supplier):
  The maintenance technicians will collect unused lids at the LISs daily and return them to Shipping & Receiving for return to the lid supplier weekly for recycling/reuse.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 56: Operational Scenarios, Stories, Use cases S5: Shelia Stores, Chief of Shipping, Receiving, & Storage (Internal)
Receiving (Jars from the Jar Supplier):
  Jars will be received from the jar supplier packaged in groups of 12 jars/box.
    Each jar is separated from the other jars by a cardboard insert.
    Each JPS conveyor belt will be supplying 960 jars to each LIS for lid installation per each 8-hour shift (one jar per 30 seconds for 8 hours).
  The Jar Supplier will combine boxes of jars on pallets moveable by a forklift, 40 boxes per pallet.
  Given there are 20 JPSs at each production facility, 1600 boxes of 12 jars will need to be supplied each shift for each production facility, for a total of 11,200 boxes per week (7 x 1600) (280 pallets)(134,400 jars) if the production facility is operating at full capacity.
  The jars delivered by the the jar supplier will have the characteristics specified in jar spec #JAR1235.
  The actual number of jars needed may vary depending on customer demand. Orders for jars will be made at least one week prior to delivery.
Storage (jars)
  The jars will be stored within the production facility in the controlled storage environment defined in Table 1. (See previous note for lids concerning the need for additional storage space, forklifts, and forklift operators for both receiving and shipping.)
Shipping (Filled jars to customers)
  Filled jars will be collected from each of the 20 JPSs, boxed 12 jars per box in the same boxes the unfilled jars were received, 40 boxes per pallet ready for customer pick up
  This results in 280 pallets to be picked up by the customers per week (40 pallets/day) at each production facility.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 57: Operational Scenarios, Stories, Use cases S6: Sally Lidisan, Lids Unlimited, Inc. (External) Lid Supplier
Providing lids to the production facilities:
  We will provide lids having the characteristics agreed to in lid spec #LID1234.
  We will make weekly deliveries of 7 days worth of lids to each facility. This results in a weekly delivery of a maximum of 134,400 lids per operating facility.
  Lids will be boxed, 48 lids per box (2,800 boxes). The boxes will be combined on pallets, 80 boxes per pallet (35 pallets).
  Key characteristics of the lids are their size, gripping locations, and maximum allowed gripping force at those locations. Lid sizes range from 2.0, 2.5, 3.0, 3.5, 4.0, 4.5 +/- .01 inches in diameter and 0.5 +/- .01” in height.
  The actual number of lids supplied will vary depending on production facility customer demand. The production facility will send us orders for number of lids to be delivered at least one week prior to delivery.
Recycling of unused lids:
  Our contract pricing assumes unused lids will be returned to us in the same boxes they arrived in for recycling/reuse.
  The recycled lids, guaranteed to spec, will then be repackaged for future delivery to the production facility.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 58: Operational Scenarios, Stories, Use cases S7: Bob Jarhead, Jars Unlimited, Inc. (External) Jar Supplier
Providing jars to the production facilities:
  We agree to provide Jars packaged in groups of 12 jars/box.
  We will combine boxes of Jars on pallets moveable by a forklift, 40 boxes per pallet.
  We will provide to each facility 11,200 boxes per week (7 x 1600) (280 pallets)(134,400 Jars) if the production facility is operating at full capacity.
  The jars delivered will have the characteristics specified in jar spec #JAR1235. Key characteristics of the jars are their size, gripping locations, maximum allowed gripping force at those locations, required lid size, and and required torque for proper installation of the lids. Jar heights vary from 3 +/- .01 inches to 8 +/- .01 inches and jar openings range from 2.0, 2.5, 3.0, 3.5, 4.0, 4.5 +/- 0.01 inches in diameter. Recommended torques are shown in Table 6.
  Delivered jars are sanitized per FDA regulations for edible food stuffs.
  The actual number of jars supplied will vary depending on production facility customer demand. The production facility will send us orders for number of jars to be delivered at least one week prior to delivery.
Recycling of unspent Jars:
  Unused jars, broken, or defective jars, will be made available for pickup and returned weekly for recycling/reuse.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 59: Operational Scenarios, Stories, Use cases S7: Bob Jarhead, Jars Unlimited, Inc. (External) Jar Supplier
Table 6 defines the recommended torques for the lids installed on glass and plastic jars. Torque is the rotational force applied during lid installation or removal from a jar. When installing a lid on the jar it is important to use the correct amount of torque to ensure a proper seal. Ideally, torque should be evenly distributed throughout the installation. Applying too little torque to a closure can increase the chances of product leakage. Over-torquing may cause some points on the lid to have more pressure than others, which could result in an improper seal as well as making it difficult for lid removal. If the lid is installed with too little torque, the jar may leak, or the lid could come off too easily. The Jars can withstand the gripping force needed to achieve the defined torque values during lid installation.
Table 6: Recommended application torque range for lid installation
Jar | Plastic | Glass
Jar opening (+/- .01 in) | Torque (in lbs) | Torque (in lbs)
2 in | 26-30 | 20-24
2.5 in | 32-36 | 26-29
3 in | 38-42 | 30-33
3.5 in | 45-49 | 36-39
4 in | 51-55 | 41-44
4.5 in | 57-62 | 46-49
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 60: Operational Scenarios, Stories, Use cases S8: Mary Safelton, Chief of Safety & Compliance (Internal)
Safety:
  The main safety concern during operations is humans in proximity of the LIRs. Because of this the entire interior of the LIS rooms is considered a keep out zone whenever the LIRs are powered on.
  Because the LIS will be handling jars with food, there are also food contamination considerations.
Human Factors:
  The LIRs need to meet all human factors standards associated with human interactions with the LIRs. This includes moving the LIRs within the facility, protection of the maintenance personnel from sharp edges or other hazards, and access to internal LIR parts subject to repair or replacement.
Compliance:
  Per OSHA, LIRs need to cease operations whenever a human is detected within the LIS room.
  Given the jars will be used for both food and chemicals, the LIRs will need to comply with all applicable FDA and EPA regulatory requirements and standards for handling food.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 61: Operational Scenarios, Stories, Use cases S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
LIR Quality Expectations
  Mean time between failures (MTBF) for each LIR is at least 3 months.
  The Mean Time to Repair (MTTR) for each LIR is 15 minutes maximum.
  Operational lifetime: 5 years with vendor recommended preventative maintenance (PM) assuming operations is 8 hours/day, 355 days/year. when the LIRs are out of the shipping containers and assembled and stored within the maintenance area in an environment defined in Table 1.
  Storage lifetime: Unlimited when stored in vendor recommended shipping containers located in a storage facility that is not climate controlled as well as when the LIRs are out of their shipping containers, assembled, powered off, and stored within the maintenance area in an environment defined in Table 1.
This Photo by Unknown Author is licensed under CC BY
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 62: Operational Scenarios, Stories, Use cases S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
General Maintainability
  The LIR needs to identify and report failures to the Line Replaceable Unit (LRU) level at power up and during operations
  The LIR supplier needs to supply assembly and PM procedures for the LIR. The PM procedure should include daily PM and monthly PM required to meet the lifetime and MTBF quality requirements.
  The LIR supplier needs to provide training required to maintain the LIRs at each production facility. Advanced training needs to be also provided to diagnose and repair failures.
  The LIR supplier needs to supply spare parts needed to repair the LIR at each production facility.
  We will send failed components to the LIR vendor for repair and/or replacement.
  The LIR supplier needs to supply at least 2 spare LIR units per production facility in case of failure or to support monthly maintenance procedures.
  The LIR supplier needs to supply a dolly on which to move the LIRs within the facility for installation and maintenance.
This Photo by Unknown Author is licensed under CC BY
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System
Requirements on the supplier will be included in the supplier SOW and contract deliverables requirements list CDRL).

## Slide 63: Operational Scenarios, Stories, Use cases S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
Initial Assembly:
  Each LIR, in their shipping crates, will be moved using a forklift to the maintenance area within the facility for unpackaging, final assembly (if needed), and to conduct tests using vendor supplied test equipment and procedures to make sure the LIR is it ready to be put into operation.
  The maintenance area is in climate-controlled area (standard office, shirt-sleeve office environment as shown in Table 1).
Movement within the production facility:
  The assembled LIRs will need to be movable by a single technician into and out of the maintenance area and into the LISs through a 3-0 door without assistance and without the need for disassembly or the use of any special equipment other than the supplier provided dolly.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 64: Operational Scenarios, Stories, Use cases S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
LIR Daily Servicing:
  Prior to each shift, a maintenance technician will obtain from storage a daily supply of lids for each LIS.
    A technician will go to each LIS and remove any unspent lids from the TBD LDS and deposit a fresh supply of lids (20 boxes/48 lids/box) into the TBD LDS.
      Lids will be removed from their boxes and placed in the TBD LDS as specified in the TBD LDS/LIR ICD.
      Lid orientations will be as specified in the LDS/LIR ICD.
    The technicians will return unspent lids to shipping & receiving who will return them the lid supplier for recycling/reuse.
    Per the LIR supplier provided daily PM procedure, the technicians will perform minor PM. This could include inspections, lubrication, and general cleaning.
    Total time for the technician at each LIS should be less than 10 minutes.
LIR Monthly Servicing:
  Per the LIR supplier provided monthly PM procedure, the technicians will perform more advanced PM for each LIR. For monthly servicing, the LIR in each LIS will be replaced with an operational spare prior to shift start and brought to the maintenance area on the supplier provided dolly. Monthly PM could include lubrication of internal parts not assessable without disassembly, replacing any limited life items recommended by the LIR supplier and general cleaning, etc.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 65: Operational Scenarios, Stories, Use cases S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
Off nominal – LIR failure:
  If a LIR fails self test pre shift or fails during the shift, the FCR C&M software will send a message to the maintenance area and shutdown the other JPS systems.
  The FCR C&M software will command the LIR to stop operations and perform a self-test and update the FCR C&M software log.
  The FCR C&M software will then issue the end-of- shift shutdown command to the LIR if possible.
  The FCR operator will contact the Maintenance Technician via intercom to provide more details about the failure.
  The FCR C&M software will provide an electronic copy of the log to the technician.
  The technician will get a functional spare LIR from the maintenance area and and move it to the LIS where the failed LIR is located using the supplier provided dolly.
  The technician will replace the failed LIR with the spare LIR, plug in the spare to a power source, connect the spare to the network (if needed), notify the FCR operator, remove the failed LIR from the LIS room, and secure the LIS door.
  The FCR operator, using the FCR C&M software, will power up the installed spare LIR, perform a self test, verify the LIR is in position, ready to install the first lid.
  If successful, the FCR operator will start the other JPS systems. When the JPS indicates a jar is in place, the FCR C&M software will notify the LIR and nominal operations will resume.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 66: Operational Scenarios, Stories, Use cases S9: “Scotty” Wrench, Chief of Maintenance & Logistics (Internal)
LIR Troubleshooting & Repair:
  The technician will return failed LIRs to the maintenance area for troubleshooting and repair.
  Using the LIR supplier provided troubleshooting and repair procedure and test equipment, a trained technician will diagnose the problem and repair if spare parts are in the inventory. If not, the technician will order the part(s) from the LIR vendor.
  Once the LIR has been repaired, it will be powered up and will perform a self-test.
  If the self test is successful, the repaired LIR will be placed in normal rotation as a spare.
  Failed components will be returned to the LIR supplier for repair, replacement, or recycling/disposal.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 67: Operational Scenarios S10: Irene Teichmann, Chief of IT (Internal)
FCR upgrades needed for FCR
  We will add a task order to the existing FCR contract to include additional computers and displays needed to command and monitor all 20 LIRs.
FCR C&M software development:
    The FCR C&M software development will be done under a separate contract from the contract for the LIR.
    Given the FCR C&M software was recently developed, tested, and is operational, the desired approach is to modify the existing FCR C&M software to apply C&M of the LIRs and new Keypads and MDS being installed in each LIS room.
    Provisions will need to be made to allow communications between the FCR C&M software and new LIRs – specifically to be able to send the “jar in place” message directly to each LIR, issue commands to the LIRs, and receive LIR health and status data.
      Other interactions between the LIRs & FCR C&M software needed to maximize automation will be defined by the software vendor.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem

## Slide 68: Operational Scenarios S10: Irene Teichmann, Chief of IT (Internal)
FCR upgrades needed for FCR
Communications between the LIR and FCR:
    Even though this is a new interface, we want the LIR to FCR C&M software communications to use similar interfaces and protocols as is used for all other JPS systems to FCR C&M software communications as defined in the JPS/FCR ICD.
    Specific commands, messages, and data parameters will have to be defined, agreed to and documented in [TBD] LIR Data Dictionary that will be added to the existing JPS/FCR ICD.
      This will require interactions between the FCR C&M software supplier and the LIR supplier. These interactions between suppliers will be put into their respective SOWs, with the LIR updates to the JPS/FCR ICD as a deliverable.
      As our integrator, River North will manage these interactions and resolve any disputes between suppliers.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem

## Slide 69
Identify Drivers and Constraints

## Slide 70: 4.3.6 Identify Drivers and Constraints
Design constraints (parts, materials, organizational design best practices, etc.).
Design standards (industry, domain, business management, business operations).
Production constraints (existing technology, facilities, equipment, cost, throughput, etc.).
Human factors (human/machine interface - HMI).
Regulations (law).
Operating environment (natural, induced).
Operating environment (social, cultural).
Existing systems: (interactions, interfaces, dependencies).
Technology Maturity.
Cost and Schedule.
Mission drivers - examples for space missions include launch date, launch vehicle performance, orbit, destination, duration, logistics, crewed/un-crewed, orbital Mechanics, etc.
Higher-level requirements allocated to the SOI. At the system level, these will be business operations level stakeholder needs and stakeholder-owned system requirements. At lower levels of the architecture, these will be requirements allocated to the SOI from the level above.
Drivers and Constraints are a major source of requirements

## Slide 71: Drivers & Constraints - Interfaces
Major constraints are interactions with external systems many of which are enabling systems
External systems are a major part of the operational environment
Interactions with external systems must be identified, defined, and addressed in the integrated set of needs and resulting design input requirements
  Of particular concern are interactions with new systems being developed concurrently with your SOI
  For the LIRs the LDS and FCR C&M Software are examples.
A major consideration are the interactions of the users, operators, maintainers, and installers with the system/product
  Referred to as Human System Integration (HSI) or Human System Engineering (HSE)
Key tools (diagrams) that can be used include:
  Context Diagram
    How does your SOI fit into the macro system it is a part (big picture view)
  External Interface Diagram
    Identify all interactions between your SOI with external systems
Failure to address all external interactions is a major reason for the system to fail system verification and system validation
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 72: Drivers & Constraints
Existing Systems
  Lids (number, size, location, torque)
  Jars (size, material,
  LIS room (space, power, environment, access)
  JPS conveyer belt system (location of jars, rate at which jars are delivered to LIS)*
  Maintenance tool set
New Systems
  Lid Dispensing System (LDS)
  LIR shipping size requirements and environments
  LIR shipping and storage environments
  LIR maintenance area
  FCR C&M Software (modified for LIR)
* Speed of conveyer belt is limited as not to move or tip over jars during stops and starts as well as the time needed to fill each jar. As a result, the maximum rate of jars presented to the LIS is one every 30 seconds – 20 seconds to get jar in place and 10 seconds stationary for lid installation.) This results in a maximum number of jars per shift per JPS is 960 and a total max per facility of 19200 jars.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 73: Existing Systems – Context Diagram (Macro system in which the LIR is a part)
JPS Conveyor belt w/filled jars
JPS Conveyor belt w/filled jars
Customer’s
Lid Supplier
Jar Supplier
LIR Supplier
Shipping & Receiving
Maintenance Area
Controlled Storage
Jars
Lids
Uncontrolled Storage
LIRs in shipping crates
JPS (20)
LIS (20)
Other JPS Systems
Facility Control Room (FCR) C&M Software
Filed Jars
Product & Labels
Unused lids
New Lids
Used Jars
Empty Jars
Failed parts
New LIRs
New Parts
New Lids
Jar Production Facility
Spare LIRs
Spare Parts
Empty Jars
Working LIRs
Failed LIRs
Commands
H&S Data
JIP Message
LIR
JIP Message
Unused lids
H&S Data
Product
Empty product containers
Labels
Labels
Product
Controlled Storage
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System
LDS
MDS
Tools

## Slide 74: LIR External Interface Diagram
LIR
LIS
Conveyer Belt System/Jars
FCR C&M Software
Shipping
Maintenance Area
Power
Space
Environment
Room layout
Fire Suppression system (FSS)
Opening to Conveyer Belt System
Commands
H&S Data, Status Msg
Maintain Test, Repair
Access, Grasp Jar,
Install Lids
JIP Msg
Operating Hours
Timing
Positioning
Jar Characteristics
People
Tools
Test Equipment
Environment
Power
Space
Handling
Access
Spare parts
Lids
Storage
Space
Environment
LIR Size/Weight
Environment
Packaging
Lid Characteristics
Access
Handling
  Data format
  Command format
  Message format
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System
LDS
Method of Access
Lids
Operational Environment includes all these external systems
External Interfaces are a major source of needs and requirements

## Slide 75: Drivers & Constraints (2)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem
Regulations
  OSHA
  EPA
  FDA
Standards
  Quality/Workmanship
  Human Systems Integration/Engineering
Project
  Schedule
  Budget
  Resources

## Slide 76: Drivers & Constraints (3)
Higher-level Needs & Requirements
  Allocated from Business Operations & Business Management levels
    Number of jars to be processed per shift per JPS
    Rate of processing jars
    Yield
Technology
  Are there existing (COTS) LIRs that can meet our needs?
  If not, what is the TRL of needed technologies?
  What is the increased cost and time to modify existing COTS or develop new robots?
  Can we change our needs such that there are COTS LIRs that can meet our needs?
Stakeholder Needs, Expectations, & Stakeholder-owned Requirements
MGOs, Measures
LIR: Lid Installing Robot; COTS: Commercial Off the Shelf; TRL: Technology Readiness Level

## Slide 77
Identify, Assess, & Handle Risk

## Slide 78: 4.3.7 Identify, Assess, and Handle Risk
As part of the elicitation activities, issues and risk must be identified and assessed.
Stakeholders should be asked specifically about any issues and risk they think could prevent the SOI to be developed and delivered within budget, schedule, or risk during its lifecycle.
Failing to address risk will result in an incomplete set of needs and resulting design input requirements resulting in a SOI that will fail system validation.
Classes of risk to be assessed and handled:
  Management risk
  Development risk
  Production risk
  System Integration, System Verification, and System Validation risk
  Compliance risk
  Operational risk
Risks to be mitigated via the SOI will be a source of needs and requirements
Traceability across the lifecycle of risks being mitigated by the SOI is critical to final system acceptance for its intended use.

## Slide 79: Operational Risk Assessment
Off-Nominal Operations (LIR or JPS)
  Start-up:
    Lids have not been supplied to the LIR LDS prior to shift start.
    Wrong size of lids supplied to the LIR LDS for the jars being presented.
    Insufficient number of lids supplied to the LIR LDS.
    LIR not able to obtain lids from the LDS
    LIR fails to power on when commanded to do so by the FCR operator.
    LIR fails its self-test.
    LIR not able to report health and status or messages to the FCR.
    LIR fails to enter “Ready to Install Lids” state.
  Shutdown:
    The LIR fails to automatically shut down at end of shift.
    The LIR fails to return a lid to the LIR LDS it may have been holding at shutdown.
    The LIR fails to notify the FCR C&M software of its shutdown status.
    The LIR internal clock is not synchronized with the facility clock.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 80: Operational Risk Assessment
Off-Nominal Operations
  LIR fails to position the LIR LHS to obtain a lid from the LIR LDS
  LIR fails to position the LIR JHS to be ready to grasp a Jar
  JPS fails to notify the FCR that a jar is in place
  FCR C&M software fails to notify the LIR the jar is in place
  The jar on the conveyer belt is not positioned per the ICD.
  Either the LIR or some other JPS system has a failure during the shift.
  The LIR LHS fails to obtain a lid
  The LIR LHS fails to install a lid
  The LHS installs a lid at an improper torque
  The JHS fails to grasp the Jar
  The JHS grasps the jar with insufficient force to keep the jar from rotating during lid installation
  The JHS grasps the jar with too much force, breaking or deforming the jar
  The JHS moves or knocks down the jar
  The Fire Suppression System within the LIS is activated
  The LIR power source fails during operations
  The operator in the control room falls asleep or is not present when a failure occurs
  Someone enters the LIS
  Problem with the FCR C&M software
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System
Each of these risks must be assessed and the
LIR role in mitigating the risk identified and reflected in the needs and resulting design input requires.

## Slide 81
Capture Preliminary Integrated Set of Lifecycle Concepts

## Slide 82: Activities Involved – part 2
From INCOSE RWG NRM

## Slide 83: 4.4 Capture Preliminary Integrated Set of Lifecycle Concepts
The results of the proceeding activities are integrated into a set of preliminary set of lifecycle concepts and supporting data.
The set of lifecycle concepts can include concepts for acquisition, development, design, verification, validation, operations, deployment, support, and retirement concepts.
These preliminary set of lifecycle concepts and supporting data and information are inputs into the lifecycle concept analysis and maturation activities.
These are preliminary in the sense that the detailed analysis concerning feasibility, completeness, consistency, and correctness has not yet been completed.
The specific lifecycle concepts used depend on the organization, its product lines, processes, and culture.
All data and information recorded within the SE tool set
Classical ConOps/OpsCon should be able to be created as a report
Must get agreement from the stakeholders before proceeding.

## Slide 84
Lifecycle Concepts Analysis and Maturation

## Slide 85: Lifecycle Concepts we need to consider
Lifecycle concepts we need to consider:
  Project management (resources, cost, schedule, customer relationships, stakeholder management.)
    Project Management Plan (PMP)
  Systems Engineering (processes, reviews, engineering team, deliverables.)
    Systems Engineering Management Plan (SEMP)
      System Verification (testing), System Validation (testing)
      Master Integration, Verification, Validation (MIVV) Plan
    Software Development & Management Plan (SDMP)
  Acquisition: contracting, SOW, SAs, contract management, acceptance.
  Product related
    Shipping, storage, assembly, operations, maintenance, disposal.
We must think beyond just operations, user interactions during operations, and just the product itself. We need to take a more holistic approach and consider the big picture and the macro system in which our SOI will operate.

## Slide 86: 4.5 Lifecycle Concepts Analysis and Maturation
The preliminary set of lifecycle concepts and supporting data and information gathered up to now are inputs into the lifecycle concept analysis and maturation activities.
Before we can define the integrated set of needs we need to do a detailed analysis concerning feasibility, completeness, consistency, and correctness of each lifecycle concept.
From INCOSE RWG NRM

## Slide 87: Feasible Lifecycle Concepts
Feasible lifecycle concepts are concepts that are proven to address the MGOs/measures and meets stakeholder expectations within the defined drivers and constraints with acceptable risk.
  Is the preliminary OpsCon/ConOps we have defined feasible?
Source of stakeholder needs that will be transformed into requirement statements for the entity (system) under development.
Diagrams and models are critical to doing the necessary analysis.
Ensure that the technical team has defined a feasible set of lifecycle concepts (ConOps/OpsCon) that has been agreed to by the stakeholders before documenting integrated set of needs and transforming them into the design input requirements.
Notes: Main Message: The ROI in doing operational concepts is extremely high. It provides the knowledge we need so we can proceed with writing requirements. Together with the other scope information, operational concepts provide the shared vision, knowledge, and a way to stay on course throughout our project life.
Avoid requirement omissions – One of the major sources of requirement defects is mission requirements. Because operational concepts address all life-cycle stages and involves the keys stakeholders, the chances of missing requirements are greatly reduced.
Allows evaluation of “what if” situations: What-if situations allow us to address both nominal and off-nominal situations. Are there alternate paths? What if some thing fails? How can we make our system more robust? What-if also allows us to explore alternate concepts and approaches and explore the use of alternate technologies. The need for trade studies is identified
Identifies Interfaces: Operational concepts bring out the interactions of your system with external systems allowing you to identify interfaces
Identifies issues/risk: Issues and risks are identified, allowing you to address these problems and resolve or mitigate them.
Brings out assumptions – a major problem is unstated and unvalidated assumptions. Operational concepts provides a mechanism for stakeholders to state their assumptions so others can validate whether the assumptions are trurl.
Increase understanding between all stakeholders: By sharing each others views, all stakeholder’s common knowledge base is expanded and all are aligned to a common vision.
Establishes a common vocabulary – We all have different backgrounds and view of the world. We all assign our own meanings to words. While developing operational concepts we can agree on common definitions for key words and put these in a project glossary
Can resolve conflicts early – By participating in the development of operational concepts, each party gains an understanding of where others are coming from and gain an common understanding of the issues.

## Slide 88: Methods to Help Define and Mature Feasible Lifecycle Concepts
Analysis
  Functional Flows
  Timeline Analysis
  Design Reference Missions
  Operational Scenarios
  Modeling/Diagrams (MBSE)
  Movies/pictures
  States and Modes Analysis
Risk Assessment
  Fault Tree Analysis
  Failure Modes & Effects Analysis (FMEA)
  Technology Risk Assessment (TRA)
Risk Mitigation
  Technology Readiness Levels (TRLs)
  Margins & Reserves
  Advancement Degree of Difficulty (AD2)
Selection of Alternatives
  Trade Studies
Demonstrations
  Animations
  Simulations
  Prototypes
  Engineering units
Notes: Main message: There are a lot of tools/methods defined in system engineering books to help you develop more complete and consistent operational concepts and requirements.
We have listed several, there are others. It is beyond the scope of this class to cover each of these in detail, our point is that they exist.
One of the things we are trying to accomplish in developing Operational Concepts is to determine what functionality is needed. To do this we need to do a functional analysis of our system. Functional analysis is the process of identifying, describing, and relating the functions a system must perform in order to fulfill its goals and objectives. Functional analysis is logically structured as a top-down hierarchical decomposition of those functions, and serves several important roles in the systems engineering process:
· To draw out all the requirements the system must meet
· To help identify measures for system effectiveness and its underlying performance or technical attributes at all levels
· To weed out from further consideration in trade studies those alternatives that cannot meet the system's goals and objectives
· To provide insights to the system-level (and below) model builders, whose mathematical models will be used in trade studies to evaluate the alternatives.
Several techniques are available to do functional analysis.
1. The primary functional analysis technique is the Functional Flow Block Diagram (FFBD). These diagrams show the network of actions that lead to the fulfillment of a function. Although the FFBD network shows the logical sequence of “what“ must happen, it does not ascribe a time duration to functions or between functions.
2. To understand time critical requirements, a Time Line Analysis (TLA) is used. A TLA can be applied to such diverse operational functions as spacecraft command sequencing and launch vehicle processing.
3. N2 diagram, which is a matrix display of functional interactions, or data flows, at a particular hierarchical level.
4. Design reference missions are like a “day in the life” scenario. How do you envision the system of interest to accomplish a given mission? How would it interact with other systems in accomplishing this mission?
5. Modeling and simulation: They say the devil is in the details. Models and simulations type it all together to help you better understand the needed behavior of your system and a more complete understanding of the needed functionality and performance.
6. Movies/pictures: A picture is worth a thousand words. Not all operational concepts need to be expressed as words. Often a picture or movie gets the concept across clearer. With today’s modeling and simulation capabilities, movies can be made of your system in action.
7. Use cases: Mainly used in the software world, use cases are great for identifying functionality needed by the system, alternate paths, exceptions, and actors (interfaces.)
We have said that your operational concepts need to address the off-nominal situations. Your goal is a more robust system. Why wait till after your system is built to do a risk assessment? Do it as part of your operational concepts. Doing fault tree analysis and FMEA will help you address risk so that you can include requirements so you can 1) eliminate the risk 2) if you can’t eliminate the risk, you can reduce its likelihood, and 3) if it does occur, reduce its consequences.
Finally, while doing your operations concepts you will identify areas where there are alternative concepts, approaches, or technologies. A major tool is selecting among multiple alternatives is trade studies, which will be our next topic.

## Slide 89: Use of Diagrams and Models for Analysis
Fundamental System Model
Functional Flow Block Diagram
SIPOC Diagram
System Architecture Diagram
From INCOSE RWG NRM

## Slide 90: Risk Assessment
Technology Risk Assessment (TRA)
  How many things are you doing for the first time?
  How many things are you doing that have been done before but in a slightly different way or different operational environment?
  For each of these things, what is the level of technical maturity? (TRL)
  What needs to be done to mature those technologies?
    Cost, schedule, resources?
Failure Modes & Effects Analysis (FMEA)
  Operational Risks
    Manufacturing (e.g, test kit)
    Customer/User (e.g., collecting sample, preparing assay)
    Instrument (e.g., performing the test)

## Slide 91: Risk Assessment
Must define nominal input and output form and characteristics
Also, must address off-nominal input and outputs
  Risk assessment – likelihood and impact of off-nominal inputs and outputs
  How will off-nominal inputs be handled?
  How can we prevent (or reduce the likelihood of) off-nominal outputs?
Include human interactions
  User/Operator/Maintainer/Disposer
From INCOSE RWG NRM

## Slide 92: Iteration to Mature Lifecycle Concepts
Doctrine of Successive Refinement – Zeroing in on a set of Feasible Concepts
From INCOSE RWG NRM

## Slide 93: LIS Conceptual/Logical Architecture
LIS
LIR Subsystems
Power
Command & Control
Structure
Thermal
Comm
Lid Dispensing System (LDS)
Lid Handling System Subsystem (LHS)
Motion Monitoring System (MMS)
Jar Holding Subsystem (JHS)
Room (space)
Power
Keypad Access
Lighting
HVAC
CCTV
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 94: LIS Hierarchical Architecture View
LDS
MMS
Room (space)
Power
Keypad Access
Lighting
HVAC
CCTV
Power
Command & Control
Structure
Thermal
Comm
LHS
JHS
LIR
LIS
JPS
Hierarchical architecture view is used in SE to flow down (allocate and budget) requirements defined at one level to the architectural parts at the next level.
FCR
Other Facility Systems
Facility
Other JPS Systems
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 95: LIR Hierarchical Architecture View
Power
C&C System
Structure
Thermal
Comm
LHS
JHS
LIR
LIS
Embedded Software is highly dependent on the hardware in which it is embedded as well as the hardware it is monitoring and controlling.
??
??
??
??
??
??
Software
Hardware
??
??
??
??
??
??
??
??
??
??
Each subsystem can be further decomposed into lower-level system elements, including the software
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 96: LIS Architecture Descriptions
Lid Dispensing System (LDS): Receives and stores daily supply of lids (960) from facility maintenance technician prior to shift start. Dispenses (makes available) lids to the LIR LHS. The LDS has not been developed yet. Specifics concerning how the LDS presents a lid to the LIR LHS is TBD. Once defined, the definition will be included in a TBD LDS/LIR ICD
Motion Monitoring System (MMS): Monitors for motion within the LIS to detect human motion. Provides health and status data and motion alerts to LIR C&M Software
Power: provides power outlets within the LIS room
Lighting: provides variable lighting within the LIS room
HVAC: distributes facility conditioned air within the LIS room. Flowrate and temperature are controllable for each LIS room via the FCR.
Room (space): Provides floor space and volume
Keypad Access: provides controlled entry to the LIS room via the door.
CCTV: cameras that allow the FCR operator to observe all activities within the LIS room.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 97: LIS Architecture Descriptions
LIR Subsystems:
  Power: Obtains power from the LIS power and distributes power within the LIR
  Structure: provides the mechanical structure to which parts are attached
  Thermal: Includes fans & venting to help control the internal temperature of parts within the LIR.
  Comm: Enables the communication between the LIR and the FCR C&M Software for supplying data and messages to the FCR C&M Software as well as the receipt of commands and messages from the FCR C&M Software.
  Command & Control (C&C): Hardware processors and software. Processes commands received from the FCR C&M Software, commands the various subsystems that make up the LIR, monitors and collects health and operational status data from the parts that make up the LIR, sends messages, and health and status data to the FCR C&M Software. Also monitors for critical failures and receives notifications from the FCR C&M Software if motion is detected.
  Lid Holding System (LHS): Obtains lids from LDS and grasps a lid with the required force and in the proper orientation to install the lid on a jar, positions lid to jar top location, and installs lids on the jars with proper torque. Provides health and status data to LIR C&C software.
  Jar Holding System (JHS): Grasps Jars and holds the jar with sufficient force to prevent the jar from rotating during lid installation, without breaking the jars. Provides health and status data to LIR C&C software.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 98: LIR Functional Analysis
Nominal Operations
  Start-up: (Initial Conditions – LIR connected to power source and communication network, LIR in power down, sleep state, ready to receive a command. LHS positioned to obtain lid from LDS, JHS in position to grasp next jar.)
    (F1) Power up LIR when “Power up” command received from FCR C&M software
    (F2) Send Power Status message to FCR C&M Software once power up is complete
    (F3) Perform self-test once power up is complete
    (F4) Send Health & Status (H&S) data to the FCR C&M Software upon completion of the self test
    (F5) Enter “Ready for Lid Installation” State upon successful completion of self-test
    (F13) Report State Change to the FCR C&M Software
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 99: LIR SIPOC Analysis – Startup
LIR C&C Software
FCR C&M Software
Send Power Status Msg Cmd
Send Power Status Msg F(2)
Powered up Status Message
FCR C&M Software
FCR C&M Software
LIR Power up Cmd
Power up LIR F(1)
Powering up Status Message
Source
Input
LIR Function
Output
Customer
LIR C&C Software
LIR C&C Software
Perform self-test Cmd
Perform LIR self-test F(3)
LIR H&S Data
Do FMEA for each input & output
FCR C&M Software
Enter Ready to Install Lid State Cmd
Enter Ready to Install Lid State F(5)
Ready to Install Lid Message
LIR C&C Software
FCR C&M Software
Send H&S Data Cmd
Send H&S Data F(4)
LIR H&S Data
FCR C&M Software
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
LIR C&C Software
FCR C&M Software
Change of State
C&C Notify Change of State F(13)
Change of State Message

## Slide 100: LIR Functional Analysis
Nominal Operations
  Lid Installation:
    (F6) LHS Obtain Lid from LDS and send “Lid Obtained” message to FCR C&M software.
    (F7) Position JHS to be ready to grasp next Jar and send “Ready to Grasp Jar” message to FCR C&M software.
    (F8) When JIP Message received from FCR C&M Software, JHS Grasp Jar and send “jar grasped” message to FCR C&M software.
    (F9) LHS Move Lid to top of Jar and send “Lid in Position” message to FCR C&M software.
    (F10) LHS Install Lid at proper torque for lid, jar size, and jar material (glass or plastic) while JHS is holding the jar from rotating and send “Lid Installed” message to FCR C&M software
    Repeat F6 – F10 until end of shift (4 pm)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JIP:” Jar in Place; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 101: LIR SIPOC Analysis – Lid Installation
FCR C&M Software
LHS Install Lid Cmd
LHS Install Lid F(10)
Lid Installed Status Message
FCR C&M Software
JIP Message;
Grasp Jar Cmd
JHS Grasp Jar F(8)
Jar Grasped Status Message
,FCR C&M Software
JHS
Position Cmd
Position JHS F(7)
JHS in position
Status Message
FCR C&M Software
Move Lid to Jar Cmd
LHS Move Lid to Jar opening F(9)
Lid in position Status Message
FCR C&M Software
Obtain lid from LDS Cmd
Obtain lid from LDS F(6)
Lid Obtained Status Message
Source(s)
Input(s)
Function
Output(s)
Customer (s)
101
Repeat F7 – F11 until end of shift
Do FMEA for each input & output
LIR C&C software
FCR C&M software,
LIR C&C software
LIR C&C software
LIR C&C software
LIR C&C software
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JIP:” Jar in Place; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 102: LIR Functional Analysis
Nominal Operations
  Concurrent functions during operations
    (F12) Monitor for commands from FCR C&M software
      Notify the FCR C&M software commands received
      There will be a separate function for the execution of each command received
    (F13) Notify the FCR if there is a change of state either as a result of the execution of a command, completion of power up or down sequence, or because of an error.
    (F3) Conduct H&S checks
    (F4) Transmit H&S data to FCR C&M software
    (F14) Monitor for Critical Failures and Alert FCR C&M software of any critical failures
      Perform end-of-shift shutdown (F15), if critical failure detected,
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 103: LIR SIPOC Analysis – Concurrent Functions
FCR C&M Software
FCR C&M Software
Commands
LIR C&C Receive Commands F(12)
Notification of Received Commands
LIR C&C Software
FCR C&M Software
Subsystems H&S Data
C&C Monitor for Critical Failure
F(14)
Critical Failure Message
Source
Input
Function
Output
Customer
103
LIR C&C Software
FCR C&M Software
Change of State
C&C Notify Change of State F(13)
Change of State Message
Continue concurrent functions until end of shift
Do FMEA for each input & output
LIR C&C Software
LIR C&C Software
Perform self-test Cmd
Perform LIR self-test F(3)
LIR H&S Data
LIR C&C Software
FCR C&M Software
Send H&S Data Cmd
Send H&S Data F(4)
LIR H&S Data
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 104: LIR Functional Analysis
Nominal Operations
  End-of-Shift Shutdown:
    (F15) Perform “End-of-Shift Shutdown” sequence automatically at 4 pm
      (F16) IF MDS is holding a Lid, Return lid to the LDS
      (F17) Position LHS to be ready to obtain a lid from LDS
      (F7) Position JHS to be ready to grasp next Jar
      (F18) Power down (sleep state, ready to accept a power up command).
      (F13) Notify the FCR C&M Software of power down state
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 105: LIR SIPOC Analysis – End of Shift Shutdown
FCR C&M software
Lid Returned to LHS
Status Message
LIR C&C software
FCR C&M software
LIR Pwr Down Cmd
LIR Power Down F(18)
LIR Powered Down,
Status Message
Source
Input
Function
Output
Customer
LIR C&C software
Return Lid to LDS Cmd
LHS Return Lid to LDS F(16)
105
FCR C&M software
JHS
Position Cmd
JHS go to Position F(7)
JHS in position
Status Message
, FCR C&M software
LHS Position Cmd
LHS go to Position F(17)
LHS in position
Status Message
LIR C&C software
LIR C&C software
FCR C&M software
Performing End-of-shift Shutdown Message
LIR Internal Clock
Time of end-of-shit
Perform end-of-shift shutdown F(15)
LIR C&C Software
FCR C&M Software
Change of State
C&C Notify Change of State F(13)
Change of State Message
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 106: LIR Functional Flow Diagram – Startup
Maintenance Technician
LDS Receive Daily Supply of Lids
Perform self-test F(3)
FCR C&M software
Power up F(1)
Enter Ready for Lid Installation State F(5)
Lids
Power up Command
Enter Lid Installation State Command
A
To Lid installation
Powered up
Status Msg
State change Status Msg
H&S Data
+
+
Pass
Supply of Lids
Send Powered up Status Msg F(2)
Send H&S Data F(4)
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Send State Change Msg F(13)
B
Concurrent Functions – Monitor for Critical Failures (F14)

## Slide 107: LIR Functional Flow Diagram – Lid Installation
A
From Startup
End of Shift?
No
Yes
D
To End of Shift
B
To Concurrent Operations
FCR C&M Software
LHS Install Lid F(10)
JHS Grasp Jar F(8)
Position JHS F(7)
LHS Move Lid to Top of Jar F(9)
LHS Obtain Lid F(6)
From Concurrent Operations
+
JIP Message
Lid Obtained Status Msg
JHS in Position Status Msg
Jar Grasped Status Msg
Lid in Position Status Msg
Lid Installed Status Msg
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JIP:” Jar in Place; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 108: LIR Functional Flow Diagram – Concurrent Operations
B
FCR C&M
Software
End of Shift?
No
Yes
D
To End of Shift
Change of State Msg
D
From Jar Lighting
Receive Commands F(12)
Monitor for Critical Failure
F(14)
Notify Change of State F(13)
Perform Self-test F(3)
To End of Shift
H&S Data
Notification of Received Commands
Critical Failure Detected Msg
A
To Lid Installation
C
C
C
C
Detection ?
Yes
C
Yes
No
Send H&S Data F(4)
H&S Data
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 109: LIR Functional Flow Diagram – End-of-Shift Operations
B
FCR FCR C&M
Ready for Power Up (F1)
From Lid Installation
A
From Concurrent Operations
D
LIR Power Down F(18)
LHS Return Lid to LDS F(16)
JHS go to Position F(7)
LHS go to Position F(17)
Perform end-of-shift shutdown F(15)
C&C Notify Change of State F(13)
Performing End-of-Shift Shutdown Msg
Lid Returned to LHS Status Msg
LHS in Position Status Msg
JHS in Position Status Msg
LIR Powered Down Status Msg
Change of State Msg
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 110
Lifecycle Concept Analysis and Maturation Progress so far………

## Slide 111: Lifecycle Concept Analysis and Maturation
So far, we have (from the functional analysis and modeling):
  Defined a notional architecture at the system and subsystem levels
  Using the SIPOC diagrams, we have a better idea of the functions, inputs, sources of inputs, outputs, and destination of the outputs.
  We should have also done FMEAs to assess risks
  We have developed functional flow block diagrams, so we have
    Confirmation of the functions to be performed
    Commands from FCR C&M Software
    Messages to/from the FCR C&M Software
    Interactions between the LIR and external systems associated with operations
  The information gained so far can be used to define system level LIR needs associated with functionality and interaction with external systems involve in operations.
This is only a small part of the information we need to define a complete integrated set of needs!

## Slide 112: A Complete Integrated Set of Needs Includes:
Function/performance
  The action or actions that your SOI must perform
  Includes both functionality and associated performance
  Primary functionally to provide the necessary capabilities
Fit
  The ability of the system to physically interface with, connect to, or become an integral part of the macro system it is a part.
  Interact with enabling systems
  Includes human system interactions and user interfaces
  Includes safety and security related functionality
Form
  Shape, size, dimensions, mass, weight and other visual parameters that uniquely distinguish a system
Quality
  ”-ilities” – reliability, availability, operability, supportability, manufacturability, maintainability, interoperability, resilience, sustainability
Compliance
  With standards and regulations

## Slide 113: Lifecycle Concept Analysis and Maturation
What we don’t have (from functional analysis and modeling):
  What software engineers call “non-functional requirements”
  Performance associated with each function
  Defined and agreed to definitions of all the interactions between the LIR and external systems associated with operations.
  Details concerning interaction with other external systems not directly associated with operations (handling, storage, shipping, maintenance, disposal).
  Characteristics of the hardware/physical systems involved in operations
    Most of the functions have both a hardware and software part in order for the function to be performed.
  Expectations for quality (-ilities) (reliability, maintainability, lifetime, availability, etc.)
  Expectations for safety and security
  Expectations for standards and regulations.
This information must also be assessed, matured, and feasibility established before we can define an integrated set of needs that is complete, consistent, correct, and feasible.

## Slide 114: Lifecycle Concept Analysis and Maturation
What we do have (from the elicitation activities):
  Expectations for quality (-ilities) (reliability, maintainability, lifetime, availability, etc.)
  Expectations for standards and regulations.
  Expanded knowledge of interactions with external systems not directly associated with operations (handling, storage, shipping, maintenance, disposal).
  Higher level expectations (goals, objectives, operation concepts, needs, allocated requirements)
What do we need to know more about?
  Feasibility (technical, cost, schedule).
  Details of the interaction between the LDS and LIR has yet to be defined.
  Communications between the LIRs and FCR C&M Software has yet to be defined.
  Specific standards and regulations
  Others??????
We can’t just rely on use cases and models – we need to address the physical aspects of the SOI, lifecycle concepts beyond just operations, as well as project management considerations

## Slide 115: Lifecycle Concept Analysis and Maturation
Approach is vastly different for:
  Standalone software applications vs embedded software or software modules that are part of a larger system.
  Subsystems and system elements that are part of a larger system being integrated by someone else.
  Systems that will be designed and manufactured inhouse vs contracting with a supplier to define, design, and build/code the system.
  Providing a supplier with an integrated set of needs vs the customer transforming those needs into customer-owned system requirements.
There is no ”one-size-fits-all” approach to product development. We need to tailor our approach to the specific SOI and approach for definition, design, build/code of the realized SOI.

## Slide 116: Lifecycle Concept Analysis and Maturation
As part of these activities, we must focus on the bigger picture and not just our SOI
From the information gathered to this point:
  We know that other parts of the facility will need to be changed.
    Shipping and receiving areas expanded due to >6 times increase in production
    LIR storage location added
    LIR maintenance facility added
    FCR C&M software updated to address the LIR
  New systems need to be procured/developed/installed/verified/validated
    Keypad system and access control for each LIS Room
    LDS in each LIS room
    MMS in each LIS room
    Other possible LIS changes: possible HVAC changes? Possible power changes?
  Contracts updated – due to increased production rate
    With Customers
    With Lid supplier
    With Jar supplier
    With Label supplier
Failing to address the larger picture will result in a failed project, even if the LIR meets all its requirements.

## Slide 117
LIR Needs Definition

## Slide 118: 4.6 Define and Record the Integrated Set of Needs
Needs are not requirements
Needs can be communicated at a higher-level of abstraction than requirements
Can organize by function, fit, form, quality, and compliance
Serves as an outline for the design input requirements transformed from the needs
Using a data-centric practice of SE, the needs will be traced to their source and to the resulting design input requirements transformed from the needs.
From INCOSE RWG NRM

## Slide 119: Needs vs Requirements
Need statements do not include the word “shall”
Examples:
  “The stakeholders need the system to ………..” or
  “The stakeholders would like the system to …….” for a goal
  Rather than “The users shall be able to ……” say “The users need to be able to ……” or “The stakeholders need the system to allow users to …………”
  Rather than “The system shall meet applicable government safety standards and regulations.” say “The stakeholders need the system to meet applicable government safety standards and regulations.”
Using these distinct formats helps make a clear distinction between needs and design input requirements.

## Slide 120: Needs vs Requirements Examples
Need statement:
  N001: The stakeholders need the LIR to be able to obtain Lids from the LDS.
Requirement statement:
  R001: The LIR shall obtain lids from the LDS as described in TBD LIR/LDS ICD.
Need statement:
  N002: The stakeholders need the LIR to install Lids of various sizes on Jars of various sizes and materials.
Requirement statements:
R003: The LIR shall install lids on the Jars using Lids having the characteristics defined in Lid Spec LID1234.
R004: The LIR shall install lids on Jars having the characteristics defined in the Jar Spec JAR1235.
Need statement:
  N003: Install Lids on Jars with the proper torque depending on lid size and jar material.
Requirement statement:
R008: The LIR shall install lids on the Jars with a torque within the torque ranges specified in Table 6.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 121
LIR Integrated Set of Needs

## Slide 122: Defining the Integrated set of Needs
Needs must be defined at the level of abstraction appropriate for need statements from the perspective of what the stakeholders need from the system or what the need the system to do.
Even though during our analysis, we dove down into the lower levels of the architecture and developed functional flow diagrams; we must move back up to the system level when defining our system level set of needs.
  No mention of subsystems, hardware components or software.
  Our needs will be transformed into system level design input requirements which will be allocated to the next level of architecture.
  At the next level of architecture, for each part of the architecture the process of defining lifecycle concepts, needs, and requirements will be repeated.
A key characteristic of needs and requirements is “Appropriate to Level”

## Slide 123: Needs – Function (functional/performance)
The stakeholders need the LIR to:
  N001: Obtain Lids from the LDS prior to shift start.
  N002: Install Lids of various sizes on Jars of various sizes and materials.
  N003: Install Lids on Jars with the proper torque depending on lid size and jar material.
  N004: Install Lids on Jars per the JPS timing.
  N005: Receive and execute commands received from the FCR C&M software.
  N006: Receive messages from the FCR C&M software
  N007: Send status messages to the FCR C&M software
  N008: Perform a self test upon power up.
These needs were derived from our functional analysis and elicitation activities
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 124: Needs – Function (functional/performance)
The stakeholders need the LIR to:
  N009: Install at least 95% of the Lids on the Jars per shift.
  N010: Monitor and health & status during operations
  N011: Report health and status data to the FCR periodically throughout the shift.
  N012: Report critical errors that occur during operations
  N013: Automatically shutdown if a critical error occurs
  N014: Report any change in system state to the FCR.
  N015: Execute the shutdown sequence automatically at the end of shift.
  Safety
  N016: Report critical system failures to the FCR.
  N017: Shutdown automatically whenever a critical system failures is detected.
  N018: Limit noise during operations such that it is not a danger to human hearing.
These needs were derived from our functional analysis and elicitation activities
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 125: Stakeholder Needs - Fit (Operations/Interfaces)
The stakeholders need the LIR to:
  N019: Operate using facility power currently available within the LISs.
  N020: Operate in the existing LIS environment.
  N021: Operate in the presence of electrical emissions existing in the existing LIS rooms.
  N022: Operate properly after being shipped in shipping crates in typical shipping environments.
  N023: Operate properly after being stored in shipping crates in an un-conditioned environment found in the existing storage location.
  N024: Continue to operate properly after being exposed to water from the fire suppression system.
These needs were derived from stakeholder elicitation activities and drivers and constraints analysis
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 126: Stakeholder Needs - Form (Physical Attributes)
The stakeholders need the LIR to:
  N025: Limit operations to within the LIS operations area shown in Figure 1.
  N026: Fit through a 3-0 (3 ft x 7ft) door without disassembly.
  N027: Allow a single maintenance technician to move an assembled LIR within the production facility without special equipment other than the supplier provided dolly.
  N028: Install lids on the jars located on the JPS conveyer belt through the opening defined in Figure 2.
These needs were derived from our stakeholder elicitation activities and drivers and constraints analysis
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System

## Slide 127: Stakeholder Needs - Quality (-ilities)
The stakeholders need the LIR to:
  Maintainability
    N029: Have a Mean time to repair (MTTR) not to exceed 15 minutes.
    N030: Identify and display failures to the Line Replaceable Unit (LRU) level.
    N031: Allow the use of common tools for repair that are currently in the maintenance area or can be easily procured from common commercial tool vendors.
    N032: Have parts, components, and assemblies that can be interchanged with the same parts, components, and assemblies in other LIRs.
  Reliability
    N033: Have a total operational lifetime of at least 5 years.
    N034: Have a Mean Time to Failure (MTTF) of no more that 3 months, assuming 8 hours/day of powered on operations.
These needs were derived from our stakeholder elicitation activities and drivers and constraints analysis
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 128: Stakeholder Needs - Quality (-ilities)
The stakeholders need the LIR to:
Shipping and Handling
    N035: Be able to be disassembled for shipment to accommodate crated the size and weight limits for shipping defined in Table 4.
    N036: Be able to survive after shipping crates have been dropped 4 feet onto a concrete surface.
These needs were derived from our stakeholder elicitation activities and drivers and constraints analysis
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 129: Stakeholder Needs - Compliance (Regulations/Standards)
The stakeholders need the LIR to:
  N037: Comply with [TBD] EPA requirements concerning the use and handling of hazardous materials
  N038: Comply with [TBD] OSHA requirements concerning human/machine interfaces
  N039: Comply with [TBD] OSHA requirements concerning the safety of humans working with robots
  N040: Comply with [TBD] FDA requirements concerning the handling of food.
  N041: Meet the requirements of MIL-STD-461E for radiated emissions.
  N042: Use power connectors for obtaining facility power that meet UL standards
  N043: Use lubricants, fluids, and fuels that meet UL 546xx non-flammability standard.
  N044: Be labeled in English.
  N045: Units of measure used for parts are English.
These needs were derived from our stakeholder elicitation activities and drivers and constraints analysis
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 130
Transformation of the LIR Integrated Set of Needs into Design Input Requirements
(System level)

## Slide 131: Transforming Needs into Design Input Requirements
The project team does requirements analysis to transform the Integrated Set of Needs into a set of Design Input Requirements, asking: “What must the SOI do to fulfill each of the needs?”
The answer will be one or more Design Input Requirements that are necessary and sufficient to meet the parent need.
The Needs-to-Requirements Transformation Matrix is one tool that can be used to aid in the transformation.
Requirements must be defined at the level of abstraction appropriate for the level the entity exists to which the requirements apply.

## Slide 132: Transforming Needs into Design Input Requirements
Even though during our analysis, we dove down into the lower levels of the architecture and developed functional flow diagrams; we must move back up to the system level when defining our system level set of Design Input Requirements.
  No mention of subsystems, hardware components, or software.
  The Design Input Requirements will be allocated to the next level of architecture.
  At the next level of architecture, for each part of the architecture the process of defining lifecycle concepts, needs, and requirements will be repeated.
    The resulting needs will be transformed into sets of Design Input Requirements for each of the entities at that level of the architecture.
    The process will repeat until the project makes a buy, reuse, or make decision.
At the system level, most of the requirements will be Ubiquitous.
A key characteristic of needs and requirements is “Appropriate to Level”

## Slide 133: LIR System Requirements – Function (functional/performance)
R001: The LIR shall obtain lids from the LDS as described in TBD LIR/LDS ICD per the timing defined in JPS ICD.
R002: The LIR shall perform a Self_Test within [TBD sec] after power up.
R003: The LIR shall install lids on the Jars using lids having the characteristics defined in Lid Spec LID1234.
R004: The LIR shall install lids on Jars having the characteristics defined in the Jar Spec JAR1235.
R005: The LIR shall install lids on Jars per the timing defined in JPS ICD.
R006: The LIR shall install lids on Jars positioned on the JPS conveyer belt as defined in the JPS ICD.
R007: The LIR shall maintain the Jar position within +/- .1 inches on the conveyer belt during lid installation.
R008: The LIR shall install lids on the Jars with a torque within the torque ranges specified in Table 6.
R009: The LIR shall install lids on Jars during the Shift defined in the JPS ICD 355 days/year.
R010: The LIR shall install a lid on a Jar within 3 sec of receiving from the FCR C&M software “Jar_in_Place” message having the characteristics defined in [TBD LIR to FCR ICD].
What the LIR must do to meet the needs
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 134: LIR System Requirements – Function (functional/performance)
R011: The LIR shall install lids on at least 99% of the Jars presented per the JPS ICD.
R012: The LIR shall Monitor System_Health_and_Status whenever the LIR is powered.
R013: The LIR shall Report System_Health_and_Status data every [TBD minutes] to the FCR C&M software as defined in [TBD LIR to FCR ICD].
R014: The LIR shall receive Commands from the FCR C&M software as defined in the [TBD LIR to FCR ICD].
R015: The LIR shall execute within [TBD sec] of receipt from the FCR C&M software, Commands defined in the [TBD LIR to FCR ICD].
R016: The LIR shall report within [TBD sec] to the FCR C&M software the completion of Commands as defined in [TBD LIR FCR ICD].
R017: The LIR shall report within [TBD sec] of occurrence, changes in System_State to the FCR C&M software as defined in [TBD LIR FCR ICD].
R018: The LIR shall synchronize its Internal_Time with the Current_Time signal received from the FCR C&M sofware defined in [TBD LIR FCR ICD].
R019: The LIR shall execute the End_of_Shift_Shutdown_Sequence within [TBD sec] of End_of_shift.
What the LIR must do to meet the needs
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 135: LIR System Requirements - Fit (Operations/Interfaces)
Power
  R020: The LIR shall operate using 110-120 VAC 60 Hz facility 30-amp power having the characteristics defined in Facility Drawing xyz.
  R021: The LIR shall obtain facility power using an EIC 320-compatible electrical standard connectors. as defined in Facility Drawing xyz.
Environment
  R022: The LIR shall meet the LIR Design Input Requirements while operating in the environment defined in Table 1.
  R023: The LIR shall meet the LIR Design Input Requirements while operating in the presence of emissions up to and including those shown in Table 2.
  R024: The LIR shall meet the LIR Design Input Requirements after being shipped in shipping crates exposed to the shipping environment defined in Table 3, for up to 24 hours.
  R025: The LIR shall meet the LIR Design Input Requirements after being stored in shipping crates exposed to the unconditioned storage environment defined in Table 5 for up to 3 years.
  R026: The LIR shall meet the LIR Design Input Requirements after being sprayed with a 15 +/- 2 gal/minute water spray and allowed to dry for no more than 24 hours.
What the LIR must do to meet the needs
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System

## Slide 136: LIR System Requirements - Fit (Operations/Interfaces)
Safety
  R027: The LIR shall report a Critical_System_Failure with in [TBD sec] to the FCR C&M software per the FCR to LIR ICD.
  R028: The LIR shall execute the End_of_Shift_Shutdown_Sequence within [TBD sec] whenever a Critical_System_Failure is detected.
  R029: The LIR shall have a time weighted average sound level less than 85 decibels measured on the A scale (slow response) or a noise dose of less than 50% in the range of 20 – 20,000 hz.
What the LIR must do to meet the needs
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.

## Slide 137: LIR System Requirements - Form (Physical Attributes)
R030: The LIR shall limit operations to within a 4-foot-wide x 16-foot-long x 8-foot-high volume within the LIS work area shown in Figure 1.
R031: The LIR shall fit through a 3-foot-wide x 7-foot-high door opening when fully assembled, and on the Supplier_Provided_Dolly without having to remove the door.
R032: The LIR shall be transportable by a single maintenance technician within the production facility without the need for special equipment other than the Supplier_Furnished_Dolly .
R033: The LIR shall install lids on the jars located on the JPS conveyer belt through the 3 ft x 3 ft +/- .1 inch opening shown in Figure 2.
What the LIR must do to meet the needs
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.

## Slide 138: LIR System Requirements - Quality (-ilities)
Reliability
  R034: The LIR shall have an operational lifetime of at least 5 years when operating per the Shift defined in the JPS ICD 355 days/year AND when maintained per (TBD Maintenance procedure xyz) AND operating in the environment defined in Table 1.
  R035: The LIR shall have a Mean Time to Failure (MTTF) of less than or equal to 720 hours of powered operations, when maintained per (TBD Maintenance procedure xyz) AND operating in the environment defined in Table 1.
Maintainability
R036: The LIR shall have a Mean Time to Repair (MTTR) not to exceed 15 minutes.
R037: The LIR shall identify and display failures to the Line Replaceable Unit (LRU) level.
R038: The LIR shall limit the use of tools needed for repair and maintenance to those listed in [TBD] document.
R039: The LIR shall have parts, components, and assemblies that can be interchanged with the same parts, components, and assemblies in other LIRs.
What the LIR must do to meet the needs
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.

## Slide 139: LIR System Requirements - Quality (-ilities)
Shipping and Handling
  R040: The LIR shall limit packaging for shipment of an unassembled LIR to the crated size and weight limits for shipping defined in Table 4.
  R041: The LIR shall meet requirements in this document after being being dropped 4 feet onto a concrete surface while unpowered and in its shipping crate or crates.
What the LIR must do to meet the needs
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.

## Slide 140: LIR System Requirements - Compliance (Regulations/Standards)
  R042: The LIR shall comply with [TBD] EPA requirements concerning the use and handling of hazardous materials.
  R043: The LIR shall comply with [TBD] OSHA requirements concerning human/machine interfaces.
  R044: The LIR shall comply with [TBD] OSHA requirements concerning the safety of humans working with robots.
  R045: The LIR shall comply with [TBD] FDA requirements concerning the handling of food.
  R046: The LIR shall meet the requirements of MIL-STD-461E for radiated emissions.
  R047: The LIR shall meet the LIR system requirements when using lubricants, fluids, and fuels that meet UL 546xx non-flammability standard.
  R048: The LIR shall use the English language for labels and displays.
  R049: The LIR shall use English units of measure.
What the LIR must do to meet the needs
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Note: parameters in the form Xyy_Zyy, are defined in the data dictionary.
Note: Must include traces to needs and other sources of the requirements.
The compliance section will consist of a lot more requirements derived from the standards and regulations expressed in a form that enables traceability across the lifecycle as to their compliance.

## Slide 141: Questions and Discussion

## Slide 142: Lou Wheatcraft
Lou Wheatcraft is a senior consultant and managing member of Wheatland Consulting, LLC. Lou is an expert in systems engineering with a focus on needs and requirements development, management, verification, & validation. Lou provides consulting and mentoring services to clients on the importance of well-formed needs & requirements helping them implement needs & requirement development and management processes, reviewing and providing comments on their needs and requirements, and helping clients write well-formed needs & requirements.
Specialties include: Understanding and documenting the problem; defining project & product scope; defining and maturing system concepts; assessing, mitigating, & managing risk; documenting stakeholder needs; transforming needs into well formed design input requirements; allocation, budgeting, and traceability; interface management, requirement management; & verification and validation.
Lou’s goal is to help clients practice better systems engineering from a needs & requirements perspective across all life cycle stages of system/product development. Getting the needs & requirements right upfront is key to a successful project. Poor needs & requirements can triple the chances of project failure.
Lou has over 50 years’ experience in systems engineering, including 22 years in the United States Air Force. Lou has taught over 200 requirement seminars over the last 21 years. Lou supports clients from all industries involved in developing and managing systems and products including aerospace, defense, medical devices, consumer goods, transportation, and energy.
Lou has spoken at Project Management Institute (PMI) chapter meetings and INCOSE conferences and chapter meetings. Lou has published and presented many papers concerning needs and requirement for NASA’s PM Challenge, INCOSE, INCOSE INSIGHT Magazine, and Crosstalk Magazine. Lou is a member of INCOSE, past Chair and current Co-Chair of the INCOSE Requirements Working Group (RWG), a member of the Project Management Institute (PMI), the Software Engineering Institute (SEI), the World Futures Society, and the National Honor Society of Pi Alpha Alpha.
Lou has a BS degree in Electrical Engineering from Oklahoma State University; an MA degree in Computer Information Systems; an MS degree in Environmental Management; and has completed the course work for an MS degree in Studies of the Future from the University of Houston – Clear Lake.