## Slide 1: Defining Well-Formed Requirements Spring 2023 Seminar Flowdown (Allocation) of Requirements
Lou Wheatcraft, Senior Consultant, Wheatland Consulting
Wheatland.consulting@gmail.com
INCOSE ChicagoLand Chapter
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 2: Flow Down of Requirements (Allocation and Budgeting)
Allocation of LIR requirements to the next level of the LIR architecture.

## Slide 3: Architectural Levels, Flow down, Allocation, & Budgeting
Unless a SOI requires no further elaboration once its set of Design Input Requirements have been defined, verified, validated, and baselined, the project team will flow the requirements down to the subsystems and system elements at the next level of the physical architecture via allocation and budgeting.
Architecting and Design Input Requirement definition go together iteratively and recursively as the project team defines the levels of the architecture.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 4: Moving Between Levels of the Physical Architecture
Requirements at one level are allocated/budgeted to the subsystems and system elements at the next level
These requirements are inputs to the lifecycle concepts, needs, and requirements definition process for each of the subsystems and system elements to which the requirements were allocated/budgeted
Process repeats until a buy, build, code, or reuse decision is made.
4
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 5: The SE Vee Model – Left Side
From INCOSE RWG NRM
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 6: The SE Vee Model – Right Side
From INCOSE RWG NRM
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 7: Allocation - Flow Down of Requirements
Based on analysis of the design input requirements and the functions of the system whose requirements are being allocated, the Architecture Definition Process decomposes the system into subsystems and system elements, resulting in the next level of the SOI physical architecture.
The allocated requirements are referred to as “parents” to the resulting “child” requirements derived to meet the intent of the allocated parent.
For each subsystem or system element that has a role in meeting the allocated parent requirement, the requirement will be allocated to those subsystems or system elements.
Allocation is the process by which the design input requirements defined for an entity at one level of the physical architecture are assigned (flow down) to the entities at the next lower level of the architecture that have a role in the implementation of the allocated requirement.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 8: LIS Requirements Flow Down
Power
C&C System
Structure
Thermal
Comm
LHS
JHS
LIR
LIS
The LIS requirements were allocated to the LIR.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Distribution System; MDS: Motion Detection System
??
??
??
??
??
??
Software
Hardware
??
??
??
??
??
??
??
??
??
??
At the LIR level, the project team defined lifecycle concepts and an Integrated Set of Needs.
These needs were transformed into a set of Design Input Requirements for the LIR.
The LIR requirements will be flowed down through allocation and budgeting to the next lower-level subsystems.

## Slide 9: Allocation using an Allocation Matrix
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Distribution System; MDS: Motion Detection System
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 10: Defining Child Requirements that Meet the Intent of the Allocated Parents.
Once the parent requirements have been allocated, they become constraints for each of the receiving entities (subsystems or system elements).
Project teams for the receiving entity will address in their lifecycle concept analysis and maturation activities, the specific “role” they play in the implementation of the intent of each of the allocated parent requirements.
The roles will be first communicated within the entity’s Integrated Set of Needs and then transformed into the entity’s set of Design Input Requirements.
The “role” must take into consideration the “role” of the other subsystems or system elements at the same level that were allocated the same parent requirement.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Distribution System; MDS: Motion Detection System
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 11: Dependencies and Interactions
Because a parent requirement is allocated to multiple entities, there is often some degree of dependency between entities.
Each of the child requirements for each of the receiving entities contribute to the realization of the allocated parent requirement.
Each of the entity project teams will need to determine their entity's specific role and how each entity will interact such that the intent of the allocated parent requirement is met.
This may involve an interaction between entities and thus an interface whose interaction must be defined and implemented.
When defining the child requirements DO NOT just copy and paste the parent requirement and change the noun.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 12: LIR External Interfaces
For each part of the architecture an external interface diagram must be developed.
For entity in which there is an interaction, each interaction must be identified, the interactions defined, and interface requirements written.
Each entity involved in the interaction will need to write complementary interface requirements.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 13: Flow Down (Allocation & Budgeting)
Power
C&C System
Structure
Thermal
Comm
LHS
JHS
LIR
LIS
Embedded Software is highly dependent on the hardware in which it is embedded as well as the hardware it is monitoring and controlling.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Distribution System; MDS: Motion Detection System
??
??
??
??
??
??
Software
Hardware
??
??
??
??
??
??
??
??
??
??
This may be a new concept for software engineers experienced in developing standalone software applications but lack experience in developing embedded software dependent on hardware systems.
It is common to have a functional/ performance requirement allocated to both hardware and software.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 14: Budgeting of Performance, Resource, and Quality Requirements
Allocation involves more than just “flowing down” requirements from one level to another. There are two types of allocation.
  Assignment of responsibility - the receiving entity has some role in meeting the intent of the allocated parent requirements.
  Allocation of some quantity - such as utilization, performance, quality, or some physical attribute.
    Physical attributes include mass, volume, power, thermal, -ilities, etc.
    Performance is associated with functional requirements in terms of how well, how fast, how many, etc. For example, accuracy, precision, time, bandwidth, or consumption of a consumable.
Budgets need to be managed and controlled at the system level.
  Results in some lower-level entities to be suboptimal in order to optimize the integrated system.
In a data-centric practice of SE budgets are managed and controlled within a model of the system.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 15: Budgeting of Performance, Resource, and Quality Requirements
A critical concept associated with budgeting is that the budgeted quantities result in requirements that have a dependency - a change in one will result in the need to change another.
Because of these dependencies, establishing traceability between the child requirements and their allocated parent as well as between peer requirements is critical.
Because of the dependencies, it is useful to view allocation of resources as an equation.
Changes to any variables on the right side of the equation will require a change in the other variables to keep the equation balanced.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 16: Traceability
The individual sets of lifecycle concepts, Integrated Set of Needs, Design Input Requirements, design output specifications, system validation artifacts, system verification artifacts do not exist in isolation, rather they represent a multi-level, 3-dimensional “spider web” of relationships which represents a data and information model of the integrated system.
These relationships are documented via links that allow the relationships to be traced between the entities that are linked both vertically across levels and horizontally across the lifecycle.
Requirements can have various types of traceability, including:
  Parent/Child
  Source
  Allocation
  Peer – Peer (Dependencies)
  Interface Definition
  Design
  System Verification
  System Validation
  Model Entity
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 17: Traceability Relationship Model
At the beginning of your project, you should choose to develop your product using a data-centric practice of SE.
A first step is selecting your SE toolset and determining what data and information will be developed and managed within the toolset.
A second step is defining a traceability relationship model addressing which relationships will be established and managed via traceability.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 18: Use of Traceability and Allocation to Manage Requirements
Combining the concepts of allocation with the concept of traceability provides the project team a powerful way to manage the design input requirements, especially across levels and across subsystems and system elements within a specific level.
As requirements are developed and flow down from one level to another, it is critical that allocation and traceability is assessed for completeness, correctness, and consistency.
These assessments are not only needed while defining the sets of design input requirements but is a major function of managing the sets of needs and sets of design input requirements, especially when assessing changes.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 19: Use of Traceability and Allocation to Manage Requirements
Common issues.
  Requirements not allocated
  Requirements not allocated correctly
  Parent requirements with no child requirements
  Needs with no implementing design input requirements
  Orphan needs that do not trace to a source.
  Orphan requirements that do not trace a need, parent, or a source
  Needs, sources, or requirements with incorrect or missing implementing child requirements.
  Requirements with an incorrect parent or source.
  Sets of child requirements are not necessary and sufficient to implement the parent requirement, need, or source from which it was transformed/derived.
This are discussed in detail within Section 14, Managing Needs and Requirements
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 20: Homework Project

## Slide 21: Homework Project
The homework project will be worked on during the 2-weeks in-between the first and final sessions.
The homework project will consist of the definition of an Integrated Set of Needs and transforming those needs into a well-formed set of Design Input Requirements for one of the LIR subsystems.
Groups will be responsible to make arrangements concerning their interaction and discussions for working on the homework project.
  It would be of great benefit if groups would team up such that one group could review and comment on the other groups sets of needs requirements.
The instructor will be available to interact with individuals and groups 1-on-1 during this 2-week period either via email or a Zoom session.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 22: LIS Conceptual/Logical Architecture
LIS
LIR Subsystems
Power
Command & Control
Structure
Thermal
Comm
Lid Dispensing System (LDS)
Lid Handling System Subsystem (LHS)
Motion Monitoring System (MMS)
Jar Handling Subsystem (JHS)
Room (space)
Power
Keypad Access
Lighting
HVAC
CCTV
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS: Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MMS: Motion Monitoring System
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 23: LIS Architecture Descriptions
LIR: Lid Installation Robot (LIR): The system that installs lids on the Jars.
Lid Dispensing System (LDS): Receives and stores daily supply of lids (960) from facility maintenance technician prior to shift start. Dispenses (makes available) lids to the LIR LHS. The LDS has not been developed yet. Specifics concerning how the LDS presents a lid to the LIR LHS is TBD. Once defined, the definition will be included in a TBD LDS/LIR ICD
Motion Detection System (MDS): Monitors for motion within the LIS to detect human motion. Provides health and status data and motion alerts to LIR C&M Software
Power: provides power outlets within the LIS room
Lighting: provides variable lighting within the LIS room
HVAC: distributes facility conditioned air within the LIS room. Flowrate and temperature are controllable for each LIS room via the FCR.
Room (space): Provides floor space and volume
Keypad Access: provides controlled entry to the LIS room via the door.
CCTV: cameras that allow the FCR operator to observe all activities within the LIS room.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Dispensing System; MDS: Motion Detection System
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 24: LIS Architecture Descriptions
LIR Subsystems:
  Power System : Obtains power from the LIS power and distributes power within the LIR
  Structure System : provides the mechanical structure to which parts are attached
  Thermal System : Includes fans & venting to help control the internal temperature of parts within the LIR.
  Comm System : Enables the communication between the LIR and the FCR C&M Software for supplying data and messages to the FCR C&M Software as well as the receipt of commands and messages from the FCR C&M Software.
  Command & Control (C&C) System: Hardware processors and software. Processes commands received from the FCR C&M Software, commands the various subsystems that make up the LIR, monitors and collects health and operational status data from the parts that make up the LIR, sends messages, and health and status data to the FCR C&M Software. Also monitors for critical failures and receives notifications from the FCR C&M Software if motion is detected.
  Lid Handling System (LHS): Obtains lids from LDS and grasps a lid with the required force and in the proper orientation to install the lid on a jar, positions lid to jar top location, and installs lids on the jars with proper torque. Provides health and status data to LIR C&C software.
  Jar Handling System (JHS): Grasps Jars and holds the jar with sufficient force to prevent the jar from rotating during lid installation, without breaking the jars. Provides health and status data to LIR C&C software.
LIS: Lid Installation System; LIR: Lid Installing Robot; JPS: Jar Processing System; FCR: Facility Control Room; JHS Jar Handling Subsystem; LHS: Lid Handling Subsystem; LDS: Lid Distribution System; MDS: Motion Detection System
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 25: A key consideration is the interaction between subsystems
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.
    Each group (or individual) will need to develop an interface diagram for their subsystem.
    Each will need to include interface requirements dealing with the interactions of their subsystems and the other subsystems they interact.
    Assume there is an internal LIR Interface Control Document (ICD) and Data Dictionary defined for the project to which your interface requirements can refer to concerning the interaction(s).
  The LIR is software intensive.
    Those focusing on software will need to interact with the groups focusing on the mechanical subsystems (Each mechanism that moves has an ECU).

## Slide 26: Homework assignment
Choose one of the LIR Subsystems
Do analysis concerning purpose of your subsystem, goals, objectives, drivers and constraints (includes allocated requirements), and risks.
  Develop an external interface diagram for your subsystem
  Identify specific interactions with each of the external systems in your external interface diagram.
Define an Integrated Set of Needs for your chosen subsystem.
Transform those needs into a set of Design Input Requirements.
  Can use Jama Software® Labs Requirements Optimizer as a digital assistant
  https://labs.jamasoftware.com/
  Can also use ChapGPT, Bard, or Bing (with caution………….)
Do requirements verification and validation activities
  Do they have the characteristics of well-formed requirements?
  Do they communicate the intent of the subsystem set of needs and allocated parent requirements?
Ideally, as time allows, it would be great if you could exchange your requirement set with another group and evaluate each other’s set of requirements.
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 27: Online Sessions
The second online session (Thursday May 11, 2023, 4 pm – 7 pm, CDT, USA) 2-4 hours as needed
  Unstructured session allowing the groups to interact with the instructor to ask questions concerning their group exercise.
  Will walk through more of the examples of poorly formed LIR requirements
  Looking for comments from the attendees concerning any of the requirements in the improved set that you want to discuss.
  Looking for comments concerning the allocation matrix and any issues you may have found with the allocations.
  Present examples you have developed and would like the instructor and class to comment on and give advice.
  While attendance is not mandatory, everyone is encouraged to attend as they will learn from the questions asked by other groups and will be able to apply what is learned to their group exercise.

## Slide 28: Online Sessions
The third online session (Saturday May 20, 2022, 8 am – 12 pm, CDT, USA) 4 hours
  Will occur the following week and will focus on the results of the group exercises, addressing attendee questions and group discussion of the concepts and outcomes of the seminar.
  Each group will do a debrief to the rest of attendees addressing the following questions:
    What squared with something that you already knew?
    What did you learn that made all the pieces fall into place?
    What did you see from a new angle?
    Based on what you learned, what will you being doing differently in the future?
    Any challenges you had or example requirements you would like to discuss?
Copyright © by Wheatland Consulting, LLC – distribution and use requires prior approval.

## Slide 29: Questions and Discussion

## Slide 30: Lou Wheatcraft
Lou Wheatcraft is a senior consultant and managing member of Wheatland Consulting, LLC. Lou is an expert in systems engineering with a focus on needs and requirements development, management, verification, & validation. Lou provides consulting and mentoring services to clients on the importance of well-formed needs & requirements helping them implement needs & requirement development and management processes, reviewing and providing comments on their needs and requirements, and helping clients write well-formed needs & requirements.
Specialties include: Understanding and documenting the problem; defining project & product scope; defining and maturing system concepts; assessing, mitigating, & managing risk; documenting needs; transforming needs into well formed design input requirements; allocation, budgeting, and traceability; interface management, requirement management; & verification and validation.
Lou’s goal is to help clients practice better systems engineering from a needs & requirements perspective across all life cycle stages of system/product development. Getting the needs & requirements right upfront is key to a successful project. Poor needs & requirements can triple the chances of project failure.
Lou has over 50 years’ experience in systems engineering, including 22 years in the United States Air Force. Lou has taught over 200 requirement seminars over the last 23 years. Lou supports clients from all industries involved in developing and managing systems and products including aerospace, defense, medical devices, consumer goods, transportation, and energy.
Lou has spoken at Project Management Institute (PMI) chapter meetings and INCOSE conferences and chapter meetings. Lou has published and presented many papers concerning needs and requirement for NASA’s PM Challenge, INCOSE, INCOSE INSIGHT Magazine, and Crosstalk Magazine. Lou is a member of INCOSE, past Chair and current Co-Chair of the INCOSE Requirements Working Group (RWG), a member of the Project Management Institute (PMI), the Software Engineering Institute (SEI), the World Futures Society, and the National Honor Society of Pi Alpha Alpha.
Lou has a BS degree in Electrical Engineering from Oklahoma State University; an MA degree in Computer Information Systems; an MS degree in Environmental Management; and has completed the course work for an MS degree in Studies of the Future from the University of Houston – Clear Lake.