## Slide 1: Reliability and Lifetime performance discussion
Lou Wheatcraft Wheatland Consulting, LLC
Copyright © 2020 by Wheatcraft. May only be used with permission

## Slide 2: Reliability and performance as a function of lifetime
Common to see requirements for reliability, lifetime, and performance as separate independent requirements
Completeness and feasibility of the requirement set
Need to write requirements to communicate stakeholder expectations.
  Reliability of what? All functions and performance? With or without periodic maintenance?
  Reliability after how much use? How many operating cycles? Under what operating conditions?
  Reliability at what point in time of a product life cycle?
  Reliability after a period of time or use?
  Dependency of reliability as a function of the level of performance? xx reliability at max performance or nominal performance? Surge capability? For how long?
What is feasible? What will be the V&V success criteria? What proof is needed?

## Slide 3: Reliability Discussion
Reliability can be difficult to specify
  Specialty SE area – requires training and experience
Reliability metrics are best stated as probability statements that are measurable by test or analysis
Need to take into account the customer usage and operating environment
  Operating environment and conditions of use need to be specified in your requirements
Time: reliability statement is incomplete without specifying the time window
Failure Definition:
  Fault tolerance: single or double fault tolerant?
  Complete failure or degradation of the product performance over time?
Confidence Level: allows for consideration of the variability of data being compared to the specification

## Slide 4: Reliability Discussion
Mean Time To Failure (MTTF) vs Mean Time Between Failures (MTBF).
  For repairable items use MTBF
  For MTBF, consider the maintenance interval
Failure rate = 1/MTBF
  “Failure rate = 0.0001 failures per hour”
  MTBF = 10,000 hours
B10 life = 10,000 hours, were Bxx refers to the time by which X% of the units in a population will have failed
90% Reliability at 10,000 hours – same as previous
  The time of interest is 10,000 hours. This could be design life, warranty period, or whatever operation/usage time is of interest to you and your customers.
90% Reliability at 10,000 hours with 90% confidence

## Slide 5: Reliability Discussion
Any time (e.g., shipping, storage, and operation) a product is subjected to stress, there is the potential for failure.
  stresses of non-operating periods can be more detrimental than those during operation.
  a product may operate in a benign environment but may need extensive protection for shipping
  many products during storage are susceptible to moisture, heat, and other environmental factors
  These factors need to be considered when developing the reliability requirements and V&V success criteria
Sources of failures: customer/user, repair, manufacturing, design

## Slide 6: Reliability Discussion
Accuracy: How close value is to required value
Precision: How close are values to each other
For some performance requirements, need to also specify the accuracy and precision requirements over time.
  Beginning of life, end of life
  Allowable degradation
What is feasible? What will be the V&V success criteria? What proof is needed?

## Slide 7: Discussion?