## Slide 1: Needs, Requirements, Verification, Validation Lifecycle Manual (NRVVLM) Overview
Requirements Working Group
Copyright © by Wheatland Consulting, LLC – permission granted to INCOSE to publish and use
Lou Wheatcraft, Senior Consultant, Wheatland Consulting, LLC
Wheatland.consulting@gmail.com

## Slide 2: The focus of this presentation

## Slide 3: Introduction
Supplements and elaborates on the INCOSE SE HB
  Provides more detailed guidance on the what, how, and why concerning needs and requirement definition and management, verification, and validation across the lifecycle.
  Addresses ambiguity and inconsistencies in ontology concerning needs and requirements definition and management, verification, and validation.
Presents systems engineering lifecycle concepts from the perspective of needs, requirements, verification, and validation (NRVV) definition and management across the system lifecycle.
To successfully complete system verification and system validation, the needs and requirements of the system as well as the system verification and system validation artifacts must be managed throughout the entire system lifecycle.
This Manual provides practical guidance on the activities required to achieve those outcomes.
“Needs, Requirements, Verification, and Validation are common threads that tie all lifecycle activities and processes together.” Lou Wheatcraft

## Slide 5: Levels of Lifecycle Concepts, Needs, & Requirements
Focus of this Manual

## Slide 6: SE Processes are Intended to be Practiced Concurrently
Concurrent definition, analysis, and maturation applied iteratively and recursively as we move down the left side of the SE Vee
Faster and cheaper than classical waterfall/serial, document-centric processes with silos
Aids in establishing correctness, completeness, and consistency, of all SE artifacts

## Slide 7: The System Engineering “Vee” Revisited
System Integration should not be thought of as only occurring on the right side of the SE Vee during IV&V
The integrated SOI must be managed from the beginning of the project across all lifecycle stages
The customer/supplier relationship must allow management of the integrated SOI

## Slide 8: Validation Across the Lifecycle
Validation should not be thought of as only occurring on the right side of the SE Vee during system integration, verification, and validation
Validation is done across the system lifecycle:
Needs
Design Input Requirements
Architecture
Design
Design Output Specifications
Realized system elements, subsystems, & the integrated SOI
Validation on the left side of the SE Vee decreases issues on the right side of the SE Vee

## Slide 9
9

## Slide 10: Design Inputs vs Design Outputs
10
The “line”

## Slide 11: Data-Centric Practice of Systems Engineering

## Slide 12: Needs vs Requirements
Needs represent the stakeholder, customer/acquirer, user view of the system
  What do the stakeholders need the system to do that will result in their problem to be solved or opportunity to be realized within defined constraints?
  Communicates the stakeholder expectations for the end-state once the System is delivered – in the end what will make the customer(s) happy?
  The system will be validated against its integrated set of needs
Requirements represent the technical, developer view of the system
  What must the system do in order to meet the needs?
  Needs are transformed into design input requirements that will result in a design that will implement that need
  The system will be verified against its design input requirements

## Slide 13
Needs, requirements, verification, and validation are the common treads that tie all SE lifecycle activities and artifacts together.
From a holist view of SE, needs, requirements, verification, and validation must be managed in the context of all other SE process areas rather than in silos distinct from the other process areas.
Rather than just focusing on the requirements, we must focus on both needs and requirements!!
Rather than just focusing on verification that the requirements are met, we must also focus on validation that the needs are met!!

## Slide 14: Levels of a System – Hierarchical View
Focus on decomposition makes it easier to develop the SOI in bite sized chunks across multiple organizational units (internal and external) based on specialize knowledge and expertise
Lifecycle concepts, needs, and requirements should be defined for the system as well as each subsystem and system element that is part of the system architecture
14

## Slide 15: Table of Contents

## Slide 16: Establish completeness, consistency, correctness, and feasibility before defining needs and transforming them into the design input requirements
Needs Before Requirements
There is a lot of work to be done BEFORE defining requirements!

## Slide 17: Lifecycle Concept and Needs Definition Part 1
17

## Slide 18: Lifecycle Concept and Needs Definition Part 2
18

## Slide 19: Use of Diagrams and Models

## Slide 20: Zeroing in on a Feasible Set of Lifecycle Concepts

## Slide 21: Defining the Integrated Set of Needs
21

## Slide 22: Table of Contents
Do the individual need expressions have the characteristics defined in the INCOSE GfWR: Necessary, Appropriate, Unambiguous, Complete, Singular, Feasible, Verifiable, Correct, and Conforming?
Does the integrated set of system needs have the characteristics defined in the INCOSE GfWR: Complete, Consistent, Feasible, Comprehensible, Able to be validated?
Have attributes been defined for each need statement?
Are all need statements traceable to their source?
Does the integrated set of system needs clearly communicate the stakeholder expectations concerning the intended use of the SOI in its operational environment by its intended users?

## Slide 23: Needs Verification and Validation
23

## Slide 24: Table of Contents

## Slide 25: Defining Design Input Requirements
25

## Slide 26: Assessing Interactions Across Interface Boundaries

## Slide 27: Moving Down the System Architecture
Requirements at one level are allocated/budgeted to the subsystems and system elements at the next level
These requirements are inputs to the lifecycle concepts, needs, and requirements definition process for each of the subsystems and system elements to which the requirements were allocated/budgeted
Process repeats until a buy, build, code, or reuse decision is made.
27

## Slide 28: Alternate Architecture for Software Centric Systems

## Slide 29: Table of Contents
Do the individual requirement expressions have the characteristics defined in the INCOSE GfWR: Necessary, Appropriate, Unambiguous, Complete, Singular, Feasible, Verifiable, Correct, and Conforming?
Does the set of design input requirements have the characteristics defined in the INCOSE GfWR: Complete, Consistent, Feasible, Comprehensible, Able to be validated?
Have attributes been defined for each requirement statement?
Are all requirement statements traceable to their parent, source, or dependent peer requirements?
Does the set of design input requirements communicate the intent of the integrated set of system needs from which they were transformed?

## Slide 30: Requirements Verification and Validation
30

## Slide 31: Table of Contents

## Slide 32: Design
32

## Slide 33: Design Verification and Validation
33

## Slide 34: Production Verification and Validation
34

## Slide 35: Table of Contents

## Slide 36: System Verification & System Validation Stages

## Slide 37: System Verification & System Validation Artifacts

## Slide 38: Sequence of System Verification & Validation Activities

## Slide 39: Table of Contents

## Slide 40: Needs, Requirements, Verification, and Validation Management
40

## Slide 41: Table of Contents

## Slide 42: Questions and Discussion